## Slide 1: Electret Microphone

## Slide 2: Condenser Microphones
Similar to electret microphones
Uses charged capacitor to generate electric signal
As diaphragm vibrates, capacitance changes resulting in electric signal
Internal battery is needed to polarize the capacitor

## Slide 3: Electret Microphone
Uses permanently charged electret material
Electret and back plate form capacitor
No polarizing voltage needed

## Slide 4: Electrets
An electret is a dielectric with a permanent electric dipole moment.
Produces electrostatic field
Made from synthetic polymers
Created by melting material, then cooling it in the presence of a strong electric field

## Slide 5: Microphone Construction

## Slide 6: Types
Diaphragm
  Electret material is used as the diaphragm of the microphone. Common and low quality
Back electret
  Electret film applied to back plate, with a diaphragm made with uncharged material
Front electret
  Electret film applied to front cover, metalized diaphragm creates the capacitor

## Slide 7: Applications
Cell phones
Computers
Hearing aids
Megaphones