## Slide 1: Chapter 1: Introduction
Our goal:
get “feel” and terminology
more depth, detail later in course
approach:
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
access net, physical media
network core
Internet/ISP structure
performance: loss, delay
protocol layers, service models
network modeling

## Slide 2: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network access and physical media
  1.4 Network core
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 3: What’s the Internet: “nuts and bolts” view
millions of connected computing devices:
  hosts = end systems
running network apps
communication links
  fiber, copper, radio, satellite
  Different transmission rates
routers: forward packets (chunks of data)
local ISP
company
network
regional ISP
router
workstation
server
mobile
Notes: What’s a human being?
Head, arm, legs, 2 eyes and eye-brows, etc.
A huge neural network capable of processing and fusing multi-modal sensor data, all running with liquid logic
A bunch of biological creatures, self organizing them into hierarchies via intangible notions of power, and eventually going back to square one with revolutions and world wars

## Slide 4: “Cool” internet appliances
World’s smallest web server
http://www-ccs.cs.umass.edu/~shri/iPic.html
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones

## Slide 5: What’s the Internet: “nuts and bolts” view
protocols coordinate communication
  Who gets to transmit?
  What path to take?
  What message format?
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet Vs private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 6: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  Web, email, games, e-commerce, file sharing
communication services provided to apps:
  Connectionless unreliable
  connection-oriented reliable
Can you give an analogy of this in real life services

## Slide 7: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet coordinated by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 8: What’s a protocol?
a human protocol and a computer network protocol:
Q: This one trivial. Can u think of a more complex case?
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time

## Slide 10: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network access and physical media
  1.4 Network core
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 11: A closer look at network structure:
network edge: applications and hosts
network core:
  routers
  network of networks
access networks, physical media: communication links

## Slide 12: The network edge:
end systems (hosts):
  run application programs
  e.g. Web, email
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal use of dedicated servers
  e.g. Skype, BitTorrent, KaZaA
Any idea how?

## Slide 14: Network edge: connection-oriented service
Goal: data transfer between end systems
Connection: prepare for data transfer ahead of time
  Request / Respond
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control:
  sender won’t overwhelm receiver
congestion control:
  senders “slow down sending rate” when network congested

## Slide 15: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]:
  connectionless
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (Web), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, DNS, Internet telephony

## Slide 16: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network access and physical media
  1.4 Network core
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 17: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 18: Residential access: point to point access
Dialup via modem
  up to 56Kbps direct access to router (often less)
  Can’t surf and phone at same time: can’t be “always on”
ADSL: asymmetric digital subscriber line
  up to 1 Mbps upstream (today typically < 256 kbps)
  up to 8 Mbps downstream (today typically < 1 Mbps)
  FDM: 50 kHz - 1 MHz for downstream
  4 kHz - 50 kHz for upstream
  0 kHz - 4 kHz for ordinary telephone

## Slide 19: Residential access: cable modems
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream, 2 Mbps upstream
network of cable and fiber attaches home to ISP router
  homes share access to router
deployment: available via cable TV companies

## Slide 20: Residential access: cable modems
Diagram: http://www.cabledatacomnews.com/cmic/diagram.html

## Slide 21: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 22: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)

## Slide 23: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 24: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM:

## Slide 25: DSL vs Cable Modem
DSL is point to point
Thus data rate does not reduce when neighbor uses his/her DSL
But, DSL uses twisted-pair, and transmission technology cannot support more than ~10Mbps
Cable Modems share the pipe to the cable headend.
Thus, your data rate can reduce when neighbors are surfing concurrently
However, fibre optic lines have significantly higher data rate (fat pipe)
Even if other users, data rate may still be higher

## Slide 26: Company access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated link connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
LANs: chapter 5

## Slide 27: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  802.11b/g (WiFi): 11 or 54 Mbps
wider-area wireless access
  provided by telco operator
  3G ~ 384 kbps
    Will it happen??
  GPRS in Europe/US
base
station
mobile
hosts
router

## Slide 28: Home networks
Typical home network components:
ADSL or cable modem
router/firewall/NAT
Ethernet
wireless access
point
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet

## Slide 29: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network access and physical media
  1.4 Network core
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 30: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 31: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required
Analogy: When president travels, a CS path set up.

## Slide 32: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 33: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 34: FDM Vs TDM
What are the tradeoffs?
  (Dis)Advantage of dividing frequency ?
  (Dis)Advantage of dividing time ?

## Slide 35: Numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!

## Slide 36: Another numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses FDM with 24 channels (frequencies)
  500 msec to establish end-to-end circuit
Let’s work it out!

## Slide 37: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
  Packets queue up
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 38: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, shared on demand  statistical multiplexing.
TDM: each host gets same slot in revolving TDM frame.
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 39: Compare
Thoughts on tradeoffs between packet switching and circuit switching?
Which one would you take?
Under what circumstances?
Why?

## Slide 40: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
Packet switching allows more users to use network!
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 41: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  simpler, no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliability, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still unsolved (chapter 7)
Is packet switching a “slam dunk winner?”
Why?

## Slide 42: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L
more on delay shortly …

## Slide 43: Packet-switched networks: forwarding
Goal: move packets through routers from source to destination
  we’ll study several path selection (routing) algorithms (chap 4)
datagram network:
  destination address in packet determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 44: Network Taxonomy
Telecommunication
networks
Circuit-switched
networks
FDM
TDM
Packet-switched
networks
Networks
with VCs
Datagram
Networks
Datagram network is not either connection-oriented
or connectionless.
Internet provides both connection-oriented (TCP) and
connectionless services (UDP) to apps.

## Slide 45: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network access and physical media
  1.4 Network core
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 46: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., MCI, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)

## Slide 47: Tier-1 ISP: e.g., Sprint
Sprint US backbone network
Seattle
Atlanta
Chicago
Roachdale
Stockton
San Jose
Anaheim
Fort Worth
Orlando
Kansas City
Cheyenne
New York
Pennsauken
Relay
Wash. DC
Tacoma
DS3 (45 Mbps)
OC3 (155 Mbps)
OC12 (622 Mbps)
OC48 (2.4 Gbps)
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence

## Slide 48: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 49: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 50: Internet structure: network of networks
a packet passes through many networks!
local (taxi)  T1 (bus)  T2 (domestic)  T3 (international)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 51: Organizing the giant structure
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 52: Turn to analogies in air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 53: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
Layers: each layer implements a service
  layers communicate with peer layers
  rely on services provided by layer below

## Slide 54: Why layering?
Explicit structure allows identification, relationship of complex system’s pieces
Modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., runway delay (wheels up time) depends on clearance of destination runway … doesn’t change the baggage tagging systems … or flight to gate assignment

## Slide 55: Protocol “Layers”
Service of each layer encapsulated
Universally agreed services called
PROTOCOLS
A large part of this course will focus on
understanding protocols for
networking systems

## Slide 56: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP, DNS …
transport: host-host data transfer
  TCP, UDP …
network: routing of datagrams from source to destination
  IP, BGP, routing protocols …
link: data transfer between neighboring network elements
  PPP, Ethernet, WiFi, Bluetooth …
physical: bits “on the wire”
  OFDM, DSSS, CDMA, Coding …
application
transport
network
link
physical

## Slide 57: Encapsulation
message
segment
datagram
frame
source
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Hl
M
router
switch

## Slide 58: Success of Layering
Protocol stack successful in Internet
Internet uses wired physical layer links
  Very reliable
  Bit Error Rate (BER) = 10-8
What about wireless networks
  Very unreliable due to channel fluctuations
  Due to co-channel interference
  Due to external noise
Does horizontal layering still hold ?

## Slide 59: Assignment # -1
Watch “City in the Sky” documentary on Netflix
You will appreciate both airline systems and
The Internet much more than you do now …

## Slide 60: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network access and physical media
  1.4 Network core
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 61: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 62: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 63: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 64: Caravan analogy
Cars “propagate” at 100 km/hr
Toll booth takes 12 sec to service a car (transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
Time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
Time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 65: Caravan analogy (more)
Cars now “propagate” at 1000 km/hr
Toll booth now takes 1 min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at 1st booth?
Yes! After 7 min, 1st car at 2nd booth and 3 cars still at 1st booth.
1st bit of packet can arrive at 2nd router before packet is fully transmitted at 1st router!
  See Ethernet applet at AWL Web site
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 66: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 67: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 68: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 69: “Real” Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link

## Slide 70: Packet loss
queue (aka buffer) preceding link has finite capacity
when packet arrives to full queue, packet is dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all

## Slide 71
Questions?

## Slide 72: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
Internet/ISP structure
performance: loss, delay
layering and service models
You now have:
context, overview, “feel” of networking
more depth, detail to follow!

## Slide 73: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
  1.3 Network core
  1.4 Network access and physical media
  1.5 Internet structure and ISPs
  1.6 Delay & loss in packet-switched networks
  1.7 Protocol layers, service models
  1.8 History

## Slide 74: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demonstration
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 75: Internet History
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 76: Internet History
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 77: Internet History
Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
Late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps

## Slide 78: Physical Media
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5: 100Mbps Ethernet

## Slide 79: Physical Media: coax, fiber
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channels on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 80: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
  11Mbps, 54 Mbps
wide-area (e.g., cellular)
  e.g. 3G: hundreds of kbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 81: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in baggage procedure doesn’t affect rest of system (as long as all baggage sections know)
layering considered harmful?