## Slide 1: Chapter 5: The Data Link Layer
Our goals:
understand principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  reliable data transfer, flow control: done!
instantiation and implementation of various link layer technologies

## Slide 2: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP

## Slide 3: Link Layer: Introduction
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
“link”
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 4: Link layer: context
Datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
Each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
travel agent = routing algorithm
transportation access = link layer protocol
Traffic lights,
Airport control,
Platform scheduling,

## Slide 5: Link Layer Services
Framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
Reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 6: Link Layer Services (more)
Flow Control:
  pacing between adjacent sending and receiving nodes
Error Detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
Error Correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
Half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 7: Adaptors Communicating
link layer implemented in “adaptor” (aka NIC)
  Ethernet card, PCMCI card, 802.11 card
sending side:
  encapsulates datagram in a frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc
  extracts datagram, passes to rcving node
adapter is semi-autonomous
link & physical layers
sending
node
frame
rcving
node
datagram
frame
adapter
adapter
link layer protocol

## Slide 8: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP
5.8 Link Virtualization: ATM

## Slide 9: Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction

## Slide 10: Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0

## Slide 11: Internet checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment (note: used at transport layer only)

## Slide 12: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP
5.8 Link Virtualization: ATM

## Slide 13: Multiple Access Links and Protocols
Two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch and host
broadcast (shared wire or medium)
  traditional Ethernet
  Bluetooth
  802.11 wireless LAN

## Slide 14: Multiple Access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 15: Ideal Multiple Access Protocol
Broadcast channel of rate R bps
1. When one node wants to transmit, it can send at rate R.
2. When M nodes want to transmit, each can send at average rate R/M
3. Fully decentralized:
  no special node to coordinate transmissions
  no synchronization of clocks, slots
4. Simple

## Slide 16: MAC Protocols: a taxonomy
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions
“Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns

## Slide 17: Channel Partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
TDM (Time Division Multiplexing): channel divided into N time slots, one per user; inefficient with low duty cycle users and at light load.
FDM (Frequency Division Multiplexing): frequency subdivided.

## Slide 18: Channel Partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
TDM (Time Division Multiplexing): channel divided into N time slots, one per user; inefficient with low duty cycle users and at light load.
FDM (Frequency Division Multiplexing): frequency subdivided.
frequency bands
time

## Slide 19: Random Access Protocols
When node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 20: Slotted ALOHA
Assumptions
all frames same size
time is divided into equal size slots, time to transmit 1 frame
nodes start to transmit frames only at beginning of slots
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
Operation
when node obtains fresh frame, it transmits in next slot
no collision, node can send new frame in next slot
if collision, node retransmits frame in each subsequent slot with prob. p until success

## Slide 21: Slotted ALOHA
Pros
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons
collisions, wasting slots
idle slots
nodes must be able to detect collision in less than time to transmit packet
clock synchronization

## Slide 22: Slotted Aloha efficiency
Suppose N nodes with many frames to send, each transmits in slot with probability p
prob that node 1 has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
For max efficiency with N nodes, find p* that maximizes Np(1-p)N-1
For many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives 1/e = .37
Efficiency is the long-run fraction of successful slots when there are many nodes, each with many frames to send
At best: channel
used for useful
transmissions 37%
of time!

## Slide 23: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 24: Pure Aloha efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0,t0+1]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n -> infty ...
= 1/(2e) = .18
Even worse !

## Slide 25: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit:
If channel sensed idle: transmit entire frame
If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!

## Slide 26: CSMA collisions
collisions can still occur:
propagation delay means
two nodes may not hear
each other’s transmission
collision:
entire packet transmission
time wasted
spatial layout of nodes
note:
role of distance & propagation delay in determining collision probability

## Slide 27: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: receiver shut off while transmitting
human analogy: the polite conversationalist

## Slide 28: CSMA/CD collision detection

## Slide 29: “Taking Turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 30: “Taking Turns” MAC protocols
Polling:
master node “invites” slave nodes to transmit in turn
concerns:
  polling overhead
  latency
  single point of failure (master)
Token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)

## Slide 31: Summary of MAC protocols
What do you do with a shared media?
  Channel Partitioning, by time, frequency or code
    Time Division, Frequency Division
  Random partitioning (dynamic),
    ALOHA, S-ALOHA, CSMA, CSMA/CD
    carrier sensing: easy in some technologies (wire), hard in others (wireless)
    CSMA/CD used in Ethernet
    CSMA/CA used in 802.11
  Taking Turns
    polling from a central site, token passing

## Slide 32: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP
5.8 Link Virtualization: ATM

## Slide 33: Ethernet
“dominant” wired LAN technology:
cheap $20 for 100Mbs!
first widely used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet
sketch

## Slide 34: Star topology
Bus topology popular through mid 90s
Now star topology prevails
Connection choices: hub or switch (more later)
hub or
switch

## Slide 35: Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates

## Slide 36: Ethernet Frame Structure (more)
Addresses: 6 bytes
  if adapter receives frame with matching destination address, or with broadcast address (eg ARP packet), it passes data in frame to net-layer protocol
  otherwise, adapter discards frame
Type: indicates the higher layer protocol (mostly IP but others may be supported such as Novell IPX and AppleTalk)
CRC: checked at receiver, if error is detected, the frame is simply dropped

## Slide 37: Unreliable, connectionless service
Connectionless: No handshaking between sending and receiving adapter.
Unreliable: receiving adapter doesn’t send acks or nacks to sending adapter
  stream of datagrams passed to network layer can have gaps
  gaps will be filled if app is using TCP
  otherwise, app will see the gaps

## Slide 38: Ethernet uses CSMA/CD
No slots
adapter doesn’t transmit if it senses that some other adapter is transmitting, that is, carrier sense
transmitting adapter aborts when it senses that another adapter is transmitting, that is, collision detection
Before attempting a retransmission, adapter waits a random time, that is, random access

## Slide 39: Ethernet CSMA/CD algorithm
1. Adaptor receives datagram from net layer & creates frame
2. If adapter senses channel idle, it starts to transmit frame. If it senses channel busy, waits until channel idle and then transmits
3. If adapter transmits entire frame without detecting another transmission, the adapter is done with frame !
4. If adapter detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, adapter enters exponential backoff: after the mth collision, adapter chooses a K at random from {0,1,2,…,2m-1}. Adapter waits K·512 bit times and returns to Step 2

## Slide 40: Question
Is it possible that:
A collision happens in Ethernet
But is not detected at the MAC layer
Remember: CSMA/CD does not use MAC layer ACKs

## Slide 41: Ethernet’s CSMA/CD (more)
Jam Signal: make sure all other transmitters are aware of collision; 48 bits
Bit time: .1 microsec for 10 Mbps Ethernet ; for K=1023, wait time is about 50 msec
Exponential Backoff:
Goal: adapt retransmission attempts to estimated current load
  heavy load: random wait will be longer
first collision: choose K from {0,1}; delay is K· 512 bit transmission times
after second collision: choose K from {0,1,2,3}…
after ten collisions, choose K from {0,1,2,3,4,…,1023}
See/interact with Java
applet on AWL Web site:
highly recommended !

## Slide 42: CSMA/CD efficiency
Tprop = max prop between 2 nodes in LAN
ttrans = time to transmit max-size frame
Efficiency goes to 1 as tprop goes to 0
Goes to 1 as ttrans goes to infinity
Much better than ALOHA, but still decentralized, simple, and cheap

## Slide 43: LAN technologies
Data link layer so far:
  services, error detection/correction, multiple access
Next: LAN technologies
  addressing
  Ethernet
  hubs, switches
  PPP

## Slide 44
Can we use the same concepts from Ethernet in wireless?

## Slide 45: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches

## Slide 46: MAC Addresses and ARP
32-bit IP address:
  network-layer address
  used to get datagram to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  used to get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs) burned in the adapter ROM

## Slide 47: LAN Addresses and ARP
Each adapter on LAN has unique LAN address
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 48: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on IP subnet to which node is attached

## Slide 49: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
knowing B’s IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
237.196.7.23
237.196.7.78
237.196.7.14
237.196.7.88

## Slide 50: ARP protocol: Same LAN (network)
A wants to send datagram to B, and B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  Dest MAC address = FF-FF-FF-FF-FF-FF
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 51: Routing to another LAN
walkthrough: send datagram from A to B via R
assume A know’s B IP address
Two ARP tables in router R, one for each IP network (LAN)
In routing table at source Host, find router 111.111.111.110
In ARP table at source, find MAC address E6-E9-00-17-BB-4B, etc
A
R
B

## Slide 52
A creates datagram with source A, destination B
A uses ARP to get R’s MAC address for 111.111.111.110
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
A’s adapter sends frame
R’s adapter receives frame
R removes IP datagram from Ethernet frame, sees its destined to B
R uses ARP to get B’s MAC address
R creates frame containing A-to-B IP datagram sends to B
A
R
B

## Slide 53: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Interconnections: Hubs and switches

## Slide 54: Interconnecting with hubs
Backbone hub interconnects LAN segments
Extends max distance between nodes
But individual segment collision domains become one large collision domain
Also, can’t interconnect 10BaseT & 100BaseT
hub
hub
hub
hub

## Slide 55: Hubs
Hubs are essentially physical-layer repeaters:
  bits coming from one link go out all other links
  at the same rate
  no frame buffering
  no CSMA/CD at hub: adapters detect collisions
  provides net management functionality
twisted pair
hub

## Slide 56: 10BaseT and 100BaseT
10/100 Mbps rate; latter called “fast ethernet”
T stands for Twisted Pair
Nodes connect to a hub: “star topology”; 100 m max distance between nodes and hub
twisted pair
hub

## Slide 57: Gbit Ethernet
uses standard Ethernet frame format
allows for point-to-point links and shared broadcast channels
in shared mode, CSMA/CD is used; short distances between nodes required for efficiency
uses hubs, called here “Buffered Distributors”
Full-Duplex at 1 Gbps for point-to-point links
10 Gbps now !

## Slide 58: Switch
Link layer device
  stores and forwards Ethernet frames
  examines frame header and selectively forwards frame based on MAC dest address
  when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 59: Forwarding
How do determine onto which LAN segment to forward frame?
Looks like a routing problem...
hub
hub
hub
switch
1
2
3

## Slide 60: Self learning
A switch has a switch table
entry in switch table:
  (MAC Address, Interface, Time Stamp)
  stale entries in table dropped (TTL can be 60 min)
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 61: Filtering/Forwarding
When switch receives a frame:
index switch table using MAC dest address
if entry found for destination then{
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 62: Switch example
Suppose C sends frame to D
Switch receives frame from C
  notes in bridge table that C is on interface 1
  because D is not in table, switch forwards frame into interfaces 2 and 3
frame received by D
hub
hub
hub
switch
A
B
C
D
E
F
G
H
I
address
interface
A
B
E
G
1
1
2
3
1
2
3

## Slide 63: Switch example
Suppose D replies back with frame to C.
Switch receives frame from from D
  notes in bridge table that D is on interface 2
  because C is in table, switch forwards frame only to interface 1
frame received by C
hub
hub
hub
switch
A
B
C
D
E
F
G
H
I
address
interface
A
B
E
G
C
1
1
2
3
1

## Slide 64: Switch: traffic isolation
switch installation breaks subnet into LAN segments
switch filters packets:
  same-LAN-segment frames not usually forwarded onto other LAN segments
  segments become separate collision domains
hub
hub
hub
switch
collision domain
collision domain
collision domain

## Slide 65: Switches: dedicated access
Switch with many interfaces
Hosts have direct connection to switch
No collisions; full duplex
Switching: A-to-A’ and B-to-B’ simultaneously, no collisions
switch
A
A’
B
B’
C
C’

## Slide 66: More on Switches
cut-through switching: frame forwarded from input to output port without first collecting entire frame
  slight reduction in latency
combinations of shared/dedicated, 10/100/1000 Mbps interfaces

## Slide 67: Institutional network
hub
hub
hub
switch
to external
network
router
IP subnet
mail server
web server

## Slide 68: So …
What’s the difference between
switches and routers?

## Slide 69: Switches vs. Routers
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms

## Slide 70: Summary comparison

## Slide 71
Questions?

## Slide 72: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP
5.8 Link Virtualization: ATM

## Slide 73: Point to Point Data Link Control
one sender, one receiver, one link: easier than broadcast link:
  no Media Access Control
  no need for explicit MAC addressing
  e.g., dialup link, ISDN line
popular point-to-point DLC protocols:
  PPP (point-to-point protocol)
  HDLC: High level data link control (Data link used to be considered “high layer” in protocol stack!

## Slide 74: PPP Design Requirements [RFC 1557]
packet framing: encapsulation of network-layer datagram in data link frame
  carry network layer data of any network layer protocol (not just IP) at same time
  ability to demultiplex upwards
bit transparency: must carry any bit pattern in the data field
error detection (no correction)
connection liveness: detect, signal link failure to network layer
network layer address negotiation: endpoint can learn/configure each other’s network address

## Slide 75: PPP non-requirements
no error correction/recovery
no flow control
out of order delivery OK
no need to support multipoint links (e.g., polling)
Error recovery, flow control, data re-ordering
all relegated to higher layers!

## Slide 76: PPP Data Frame
Flag: delimiter (framing)
Address: does nothing (only one option)
Control: does nothing; in the future possible multiple control fields
Protocol: upper layer protocol to which frame delivered (eg, PPP-LCP, IP, IPCP, etc)

## Slide 77: PPP Data Frame
info: upper layer data being carried
check: cyclic redundancy check for error detection

## Slide 78: Byte Stuffing
“data transparency” requirement: data field must be allowed to include flag pattern <01111110>
  Q: is received <01111110> data or flag?
Sender: adds (“stuffs”) extra < 01111110> byte after each < 01111110> data byte
Receiver:
  two 01111110 bytes in a row: discard first byte, continue data reception
  single 01111110: flag byte

## Slide 79: Byte Stuffing
flag byte
pattern
in data
to send
flag byte pattern plus
stuffed byte in transmitted data

## Slide 80: PPP Data Control Protocol
Before exchanging network-layer data, data link peers must
configure PPP link (max. frame length, authentication)
learn/configure network
layer information
  for IP: carry IP Control Protocol (IPCP) msgs (protocol field: 8021) to configure/learn IP address

## Slide 81: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-Layer Addressing
5.5 Ethernet
5.6 Hubs and switches
5.7 PPP
5.8 Link Virtualization: ATM and MPLS

## Slide 82: Virtualization of networks
Virtualization of resources: a powerful abstraction in systems engineering:
computing examples: virtual memory, virtual devices
  Virtual machines: e.g., java
  IBM VM os from 1960’s/70’s
layering of abstractions: don’t sweat the details of the lower layer, only deal with lower layers abstractly

## Slide 83: The Internet: virtualizing networks
1974: multiple unconnected nets
  ARPAnet
  data-over-cable networks
  packet satellite network (Aloha)
  packet radio network
… differing in:
  addressing conventions
  packet formats
  error recovery
  routing
ARPAnet
satellite net
"A Protocol for Packet Network Intercommunication",
V. Cerf, R. Kahn, IEEE Transactions on Communications,
May, 1974, pp. 637-648.

## Slide 84: The Internet: virtualizing networks
ARPAnet
satellite net
gateway
Internetwork layer (IP):
addressing: internetwork appears as a single, uniform entity, despite underlying local network heterogeneity
network of networks
Gateway:
“embed internetwork packets in local packet format or extract them”
route (at internetwork level) to next gateway

## Slide 85: Cerf & Kahn’s Internetwork Architecture
What is virtualized?
two layers of addressing: internetwork and local network
new layer (IP) makes everything homogeneous at internetwork layer
underlying local network technology
  cable
  satellite
  56K telephone modem
  today: ATM, MPLS
… “invisible” at internetwork layer. Looks like a link layer technology to IP!

## Slide 86: ATM and MPLS
ATM, MPLS separate networks in their own right
  different service models, addressing, routing from Internet
viewed by Internet as logical link connecting IP routers
  just like dialup link is really part of separate network (telephone network)
ATM, MPSL: of technical interest in their own right

## Slide 87: Asynchronous Transfer Mode: ATM
1990’s/00 standard for high-speed (155Mbps to 622 Mbps and higher) Broadband Integrated Service Digital Network architecture
Goal: integrated, end-end transport to carry voice, video, data
  meeting timing/QoS requirements of voice, video (versus Internet best-effort model)
  “next generation” telephony:
  packet-switching (fixed length packets, called “cells”) using virtual circuits

## Slide 88: ATM architecture
adaptation layer: only at edge of ATM network
  data segmentation/reassembly
  roughly analagous to Internet transport layer
ATM layer: “network” layer
  cell switching, routing
physical layer

## Slide 89: ATM: network or link layer?
Vision: end-to-end transport: “ATM from desktop to desktop”
  ATM is a network technology
Reality: used to connect IP backbone routers
  “IP over ATM”
  ATM as switched link layer, connecting IP routers
ATM
network
IP
network

## Slide 90: ATM Adaptation Layer (AAL)
ATM Adaptation Layer (AAL): “adapts” upper layers (IP or native ATM applications) to ATM layer below
AAL present only in end systems, not in switches
AAL layer segment (header/trailer fields, data) fragmented across multiple ATM cells
  analogy: TCP segment in many IP packets

## Slide 91: ATM Layer: Virtual Circuits
VC transport: cells carried on VC from source to dest
  call setup, teardown for each call before data can flow
  each packet carries VC identifier (not destination ID)
  every switch on source-dest path maintain “state” for each passing connection
  link,switch resources (bandwidth, buffers) may be allocated to VC: to get circuit-like perf.
Permanent VCs (PVCs)
  long lasting connections
  typically: “permanent” route between two IP routers
Switched VCs (SVC):
  dynamically set up on per-call basis

## Slide 92: ATM VCs
Advantages of ATM VC approach:
  QoS performance guarantee for connection mapped to VC (bandwidth, delay, delay jitter)
Drawbacks of ATM VC approach:
  Inefficient support of datagram traffic
  SVC introduces call setup latency, processing overhead for short lived connections

## Slide 93: ATM Layer: ATM cell
5-byte ATM cell header
48-byte payload
  Why?: small payload -> short cell-creation delay for digitized voice
  halfway between 32 and 64 (compromise!)
Cell header
Cell format

## Slide 94: ATM cell header
VCI: virtual channel ID
  will change from link to link thru net
PT: Payload type (e.g. RM cell versus data cell)
CLP: Cell Loss Priority bit
  CLP = 1 implies low priority cell, can be discarded if congestion
HEC: Header Error Checksum
  cyclic redundancy check

## Slide 95: IP-Over-ATM
Classic IP only
3 “networks” (e.g., LAN segments)
MAC (802.3) and IP addresses
IP over ATM
replace “network” (e.g., LAN segment) with ATM network
ATM addresses, IP addresses
ATM
network
Ethernet
LANs
Ethernet
LANs

## Slide 96: IP-Over-ATM
AAL
ATM
phy
phy
Eth
IP
ATM
phy
ATM
phy
app
transport
IP
AAL
ATM
phy
app
transport
IP
Eth
phy

## Slide 97: Datagram Journey in IP-over-ATM Network
at Source Host:
  IP layer maps between IP, ATM dest address (using ARP)
  passes datagram to AAL5
  AAL5 encapsulates data, segments cells, passes to ATM layer
ATM network: moves cell along VC to destination
at Destination Host:
  AAL5 reassembles cells into original datagram
  if CRC OK, datagram is passed to IP

## Slide 98: Multiprotocol label switching (MPLS)
initial goal: speed up IP forwarding by using fixed length label (instead of IP address) to do forwarding
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
5

## Slide 99: MPLS capable routers
a.k.a. label-switched router
forwards packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
signaling protocol needed to set up forwarding
  RSVP-TE
  forwarding possible along paths that IP alone would not allow (e.g., source-specific routing) !!
  use MPLS for traffic engineering

## Slide 100: MPLS forwarding tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1

## Slide 101: Chapter 5: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS
  PPP
  virtualized networks as a link layer: ATM, MPLS

## Slide 102: ATM Physical Layer (more)
Two pieces (sublayers) of physical layer:
Transmission Convergence Sublayer (TCS): adapts ATM layer above to PMD sublayer below
Physical Medium Dependent: depends on physical medium being used
TCS Functions:
  Header checksum generation: 8 bits CRC
  Cell delineation
  With “unstructured” PMD sublayer, transmission of idle cells when no data cells to send

## Slide 103: ATM Physical Layer
Physical Medium Dependent (PMD) sublayer
SONET/SDH: transmission frame structure (like a container carrying bits);
  bit synchronization;
  bandwidth partitions (TDM);
  several speeds: OC3 = 155.52 Mbps; OC12 = 622.08 Mbps; OC48 = 2.45 Gbps, OC192 = 9.6 Gbps
TI/T3: transmission frame structure (old telephone hierarchy): 1.5 Mbps/ 45 Mbps
unstructured: just cells (busy/idle)

## Slide 104: Manchester encoding
Used in 10BaseT
Each bit has a transition
Allows clocks in sending and receiving nodes to synchronize to each other
  no need for a centralized, global clock among nodes!
Hey, this is physical-layer stuff!

## Slide 105: Checksumming: Cyclic Redundancy Check
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice

## Slide 106: CRC Example
Want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R
R = remainder[ ]
D.2r
G

## Slide 107: ATM Adaptation Layer (AAL) [more]
Different versions of AAL layers, depending on ATM service class:
AAL1: for CBR (Constant Bit Rate) services, e.g. circuit emulation
AAL2: for VBR (Variable Bit Rate) services, e.g., MPEG video
AAL5: for data (eg, IP datagrams)
AAL PDU
ATM cell
User data

## Slide 108: ATM Layer
Service: transport cells across ATM network
analogous to IP network layer
very different services than IP network layer
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?

## Slide 109: IP-Over-ATM
Issues:
IP datagrams into ATM AAL5 PDUs
from IP addresses to ATM addresses
  just like IP addresses to 802.3 MAC addresses!
ATM
network
Ethernet
LANs