## Slide 1: Socket Programming (MP1-)
Presented by Wally

## Slide 2: Socket programming
Socket API
introduced in BSD4.1 UNIX, 1981
explicitly created, used, released by apps
client/server paradigm
two types of transport service via socket API:
  unreliable datagram
  reliable, byte stream-oriented
a host-local,
application-created,
OS-controlled interface (a “door”) into which
application process can both send and
receive messages to/from another application process
socket
Goal: learn how to build client/server application that communicate using sockets

## Slide 3: Socket-programming using TCP
Socket: a door between application process and end-end-transport protocol (UCP or TCP)
TCP service: reliable transfer of bytes from one process to another
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
internet

## Slide 4: Socket programming: Terminology
Term | Format | Example | Analogy-phone
IP(v4) | x.x.x.x | 192.168.0.1 | Phone number
Port | N<65535 | 80 | Extension #
Socket | [memory/ resource] | s=socket(…) | Physical phone

## Slide 5: Client/server socket interaction: TCP
Server (stand-by, waiting for requests)
Client (initiate the request)
Create socket
(Claim resources/ available phone)
Bind port
(Claim ID on this machine/
get a phone extension No.)
Listen/ accept
(Wait for connections/ Wait for phone call)
Send/ receive
(Communication/ Chat on phone)
Create socket
(Claim resources/ available phone)
Connect
(connect to server/ call others)
-
(Don’t care about public port/ phone #)
Send/ receive
(Communication/ Chat on phone)
Close socket
(End communication/ Hang up the phone)
Close socket
(End communication/ Hang up the phone)
Red word: wait for the other side

## Slide 6: Client/server socket interaction: TCP
Server (stand-by, waiting for requests)
Client (initiate the request)
Create socket
(Claim resources/ available phone)
Bind port
(Claim ID on this machine/
get a phone extension No.)
Listen/ accept
(Wait for connections/ Wait for phone call)
Send/ receive
(Communication/ Chat on phone)
Create socket
(Claim resources/ available phone)
Connect
(connect to server/ call others)
-
(Don’t care about public port/ phone #)
Send/ receive
(Communication/ Chat on phone)
Close socket
(End communication/ Hang up the phone)
Close socket
(End communication/ Hang up the phone)
1
2
3
4
5
6
6
7/8
7/8
Red word: wait for the other side

## Slide 7: Socket programming with TCP
Client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact
Client contacts server by:
creating client-local TCP socket
specifying IP address, port number of server process
When client creates socket: client TCP establishes connection to server TCP
When contacted by client, server TCP creates new socket for server process to communicate with client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients (more in Chap 3)
TCP provides reliable, in-order
transfer of bytes (“pipe”)
between client and server
application viewpoint

## Slide 8: Client/server socket interaction: TCP
Server (stand-by, waiting for requests)
Client (initiate the request)
Create socket
(Claim resources/ available phone)
Bind port
(Claim ID on this machine/
get a phone extension No.)
Listen/ accept
Send/ receive
(Communication/ Chat on phone)
Create socket
(Claim resources/ available phone)
Connect
(connect to server/ call others)
Send/ receive
(Communication/ Chat on phone)
Close socket
(End communication/ Hang up the phone)
Close socket
(End communication/ Hang up the phone)
Fork/ New thread
Child
Parent

## Slide 9: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data from multiple
sockets, enveloping data with
header (later used for
demultiplexing)
Multiplexing at send host:

## Slide 10: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format
Analogous to airport shuttles
Shuttles MUX passengers and take them
to downtown -- DeMUX at different locations

## Slide 11: Connectionless demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(99111);
DatagramSocket mySocket2 = new DatagramSocket(99222);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 12: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”

## Slide 13: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 14: Connection-oriented demux (cont)
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B
= process
= socket

## Slide 15: Connection-oriented demux: Threaded Web Server
Client
IP:B
P1
client
IP: A
P1
P2
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P4
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B
= process
= socket