## Slide 1: Stepping through Routing Algorithms
Ashutosh Dhekne
ECE/CS 438 - Communication Networks
Fall 2018
University of Illinois at Urbana-Champaign

## Slide 2: Dijkstra’s Algorithm
Needs the global topology as input.
Every router computes its own routing table from this global view
We will follow Dijkstra’s algorithm for router a in this topology:
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13

## Slide 3
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -

## Slide 4
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
Which neighbor will we pick next?

## Slide 5
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -

## Slide 6
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -
2 | abc |  |  | 3,a | ?,? | ∞, - | 3,c

## Slide 7
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -
2 | abc |  |  | 3,a | 12,c | ∞, - | 3,c

## Slide 8
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -
2 | abc |  |  | 3,a | 12,c | ∞, - | 3,c
3 | abcd |  |  |  | 7,d | ∞, - | 3,c

## Slide 9
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -
2 | abc |  |  | 3,a | 12,c | ∞, - | 3,c
3 | abcd |  |  |  | 7,d | ∞, - | 3,c
4 | abcdg |  |  |  | 7,d | 4,g | 

## Slide 10
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -
2 | abc |  |  | 3,a | 12,c | ∞, - | 3,c
3 | abcd |  |  |  | 7,d | ∞, - | 3,c
4 | abcdg |  |  |  | 7,d | 4,g | 
5 | abcdgf |  |  |  | 5,f |  | 

## Slide 11
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -
2 | abc |  |  | 3,a | 12,c | ∞, - | 3,c
3 | abcd |  |  |  | 7,d | ∞, - | 3,c
4 | abcdg |  |  |  | 7,d | 4,g | 
5 | abcdgf |  |  |  | 5,f |  | 
6 | abcdgfe |  |  |  |  |  | 

## Slide 12
a
b
c
d
e
f
g
1
2
3
1
1
1
Step | N’ | D(b),p(b) | D(c),p(c) | D(d),p(d) | D(e),p(e) | D(f),p(f) | D(g),p(g)
0 | a | 1,a | 2,a | 3,a | ∞, - | ∞, - | ∞, -
1 | ab |  | 2,a | 3,a | ∞, - | ∞, - | ∞, -
2 | abc |  |  | 3,a | 12,c | ∞, - | 3,c
3 | abcd |  |  |  | 7,d | ∞, - | 3,c
4 | abcdg |  |  |  | 7,d | 4,g | 
5 | abcdgf |  |  |  | 5,f |  | 
6 | abcdgfe |  |  |  |  |  | 

## Slide 13: Bellman-Ford Distance Vector Algorithm
Relies only on knowledge obtained from neighbors and own links
Every router computes its own routing tables but propagates the routing table to others
We will follow part of Bellman-Ford algorithm at routers a and c in this topology:
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13

## Slide 14
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
 | a | b | c | d | e | f | g
a | 0,a | 1,a | 2,a | 3,a | ∞ | ∞ | ∞
b |  |  |  |  |  |  | 
c |  |  |  |  |  |  | 
d |  |  |  |  |  |  | 
e |  |  |  |  |  |  | 
f |  |  |  |  |  |  | 
g |  |  |  |  |  |  | 
a’s DV

## Slide 15
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
 | a | b | c | d | e | f | g
a | 0,a | 1,a | 2,a | 3,a | ∞ | ∞ | ∞
b | 1 | 0 | 13 | ∞ | ∞ | ∞ | ∞
c | 2 | 13 | 0 | ∞ | 10 | ∞ | 1
d | 3 | ∞ | ∞ | 0 | 4 | ∞ | ∞
e | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
f | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
g | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
a’s DV
After a receives all DVs from its neighbors (part 1)

## Slide 16
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
 | a | b | c | d | e | f | g
a | 0,a | 1,a | 2,a | 3,a | 7,d | ∞ | 3,c
b | 1 | 0 | 13 | ∞ | ∞ | ∞ | ∞
c | 2 | 13 | 0 | ∞ | 10 | ∞ | 1
d | 3 | ∞ | ∞ | 0 | 4 | ∞ | ∞
e | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
f | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
g | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
a’s DV
After a corrects its own DV based on its neighbors (part 2)

## Slide 17
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
 | a | b | c | d | e | f | g
a | 0 | 1 | 2 | 3 | ∞ | ∞ | ∞
b | 1 | 0 | 13 | ∞ | ∞ | ∞ | ∞
c | 2,a | 13,b | 0,c | ∞ | 10,c | ∞ | 1,c
d | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
e | ∞ | ∞ | 10 | 4 | 0 | 1 | 5
f | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
g | ∞ | ∞ | 1 | ∞ | 5 | 1 | 0
c’s DV
After c receives all DVs from its neighbors (part 1)

## Slide 18
 | a | b | c | d | e | f | g
a | 0 | 1 | 2 | 3 | ∞ | ∞ | ∞
b | 1 | 0 | 13 | ∞ | ∞ | ∞ | ∞
c | 2,c | 3,a | 0 | ∞ | 6,g | ∞ | 1,c
d | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
e | ∞ | ∞ | 10 | 4 | 0 | 1 | 5
f | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
g | ∞ | ∞ | 1 | ∞ | 5 | 1 | 0
c’s DV
After c updates its DVs for its neighbors (part 2)
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13

## Slide 19
 | a | b | c | d | e | f | g
a | 0 | 1 | 2 | 3 | ∞ | ∞ | ∞
b | 1 | 0 | 13 | ∞ | ∞ | ∞ | ∞
c | 2,c | 3,a | 0,c | 5,a | 6,g | 2,g | 1,c
d | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
e | ∞ | ∞ | 10 | 4 | 0 | 1 | 5
f | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
g | ∞ | ∞ | 1 | ∞ | 5 | 1 | 0
c’s DV
After c updates its DVs for everyone else (part 3)
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13

## Slide 20
What does c send to a?
Consider poisoned reverse

## Slide 21
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
 | a | b | c | d | e | f | g
a | 0,a | 1,a | 2,a | 3,a | 7,d | ∞ | 3,c
b | 1 | 0 | 13 | ∞ | ∞ | ∞ | ∞
c | 2 | ∞ | 0 | ∞ | 6 | 2 | 1
d | 3 | ∞ | ∞ | 0 | 4 | ∞ | ∞
e | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
f | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
g | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
a’s DV
After a receives DV from c
Poisoned Reverse

## Slide 22
a
b
c
d
e
f
g
1
2
3
4
1
1
1
10
5
13
 | a | b | c | d | e | f | g
a | 0,a | 1,a | 2,a | 3,a | 7,d | 4,c | 3,c
b | 1 | 0 | 13 | ∞ | ∞ | ∞ | ∞
c | 2 | ∞ | 0 | ∞ | 6 | 2 | 1
d | 3 | ∞ | ∞ | 0 | 4 | ∞ | ∞
e | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
f | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
g | ∞ | ∞ | ∞ | ∞ | ∞ | ∞ | ∞
a’s DV
After a receives DV from c
Affects a’s DV

## Slide 23: UIUC’s connection to the rest of the world
Concepts to recall:
  Autonomous Systems – all routers under one administrative control
  Routers are connected to each other by physical links.
  Each AS can have large number of routers, NAT boxes, and hosts
  AS numbers are given out by IANA

## Slide 24: UIUC ASs
UIUC – AS38
UIUC – AS40387
UIUC – AS698
AS38
AS40387
AS698
AS293
Es.net
AS11537
Internet2.edu
Many others
AS23473
pavlovmedia.com
AS6939
He.net
Many others
Many others
Many others

## Slide 25: Example global AS – Hurricane Electric
Source: http://he.net/HurricaneElectricNetworkMap.pdf

## Slide 26
Intra-AS routing focuses on performance,
Inter-AS routing focuses on policy
But even intra-AS can be a world-wide network of routers!
Example global AS – Hurricane Electric
Source: http://he.net/HurricaneElectricNetworkMap.pdf