## Slide 1: ECE 333 Renewable Energy Systems
Lecture 9: Photovoltaic Materials and Electrical Characteristics
Dr. Karl Reinhard
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign
reinhrd2@illinois.edu

## Slide 2: Announcements
HW 4 is due on Thursday, 15 Feb
Quiz 4 on Thursday 15 Feb.
Read Chapter 5 (Photovoltaic Materials and Electrical Characteristics)
Report 2 due Thursday 15 Feb.

## Slide 3: Total Clear Sky Insolation
The total insolation is the sum of the direct beam, diffuse and reflected
  Most is direct beam; models for diffuse and reflected are more approximate (and certainly site dependent)
Superscript h indicates values on surface in front of collector; r is estimates reflectivity of surface, ranging from 0.8 for snow to 0.1 for dark shingles
q is angle between sun and normal to collector

## Slide 4: Photovoltaics (PV)
Photovoltaic definition- a material or device that is capable of converting the energy contained in photons of light into an electrical voltage and current
PV serving village health center, West Bengal, India
http://www1.eere.energy.gov/solar/pv_use.html
"Sojourner" exploring Mars, 1997
UIUC Solar Decathalon House – 2nd place overall in 2009
http://www.solardecathlon.uiuc.edu/gallery.html#

## Slide 5: PV History – Edmond Becquerel
Edmond Becquerel (1820 – 1891), French physicist
Studied solar spectrum, magnetism, electricity, and optics.
Observed / documented the photovoltaic effect, in 1839 (age 19)
Generated electricity by illuminating an electrode with different types of light, including sunlight
  ( https://en.wikipedia.org/wiki/Edmond_Becquerel accessed 9 Feb 18 )
Diagram of Becquerel’s Apparatus
http://www.pveducation.org/pvcdrom/manufacturing/first-photovoltaic-devices accessed 9 Feb 18

## Slide 6: PV History – Willoughby Smith
Willoughby Smith (1828 – 1891), English Elect Engr
Discovered selenium’s (Se) photoconductive behavior
Worked for the Gutta Percha Company, which manufactured telegraph wires – including underwater cables
Gutta-percha tree (Malayan for “percha latex”) sap is a natural latex elastomer – a good insulator https://en.wikipedia.org/wiki/Gutta-percha
In 1873, Smith developed a method in the lab for continually testing an underwater cable as it was being laid using Se rods
However inconsistent results in practice; discovered that the Se rod  increased significantly when exposed to strong light
Smith published "Effect of Light on Selenium during the passage of an Electric Current" in Nature Magazine, Feb 1873
(https://en.wikipedia.org/wiki/Willoughby_Smith accessed 9 Feb 18 )

## Slide 7: PV History – Adams and Day
William Grylls Adams, Professor, (1836-1915)
and student Richard Evans Day @ King’s College
Were experimenting with Se
Following Smith’s1873 report, they investigated photoelectric effects
In 1876, demonstrated Se’s photovoltaic behavior
https://www.popsci.com/article/science/invention-solar-cell#page-2 accessed 9 Feb 18
http://www.pveducation.org/pvcdrom/manufacturing/first-photovoltaic-devices
William Grylls Adams

## Slide 8: PV History – Albert Einstein
Albert Einstein, Theoretical Physicist, (1879 - 1955)
1905 published 4 Groundbreaking Papers
  Photoelectric Effect (Nobel Prize in Physics 1921)
  Brownian motion
  Special relativity
  Equivalence of mass and energy
Photoelectric Effect
  Light occurs packets of energy, quanta (i.e. photons)
  Light quanta power varies according to the light’s wavelength – shorter the wavelength, the more power
  Provided scientific framework to “photoelectricity”
  Explained the photoelectric phenomenon in scientific terms
https://www.popsci.com/article/science/invention-solar-cell#page-2
https://en.wikipedia.org/wiki/Albert_Einstein

## Slide 9: PV History – Jan Czochralski
Jan Czochralski, Polish Chemist, (1885 – 1953)
Developed the Czochralski Process for growing single crystals (1915)  semiconductor wafer production
Accidental discovery – instead of dipping his pen into the inkwell, he did so in molten tin and drew a tin filament, that later proved to be a single crystal.
(https://en.wikipedia.org/wiki/Jan_Czochralski)
https://strgmbh.de/melt/100-mm-cz-si/
https://en.wikipedia.org/wiki/Czochralski_process

## Slide 10
https://energy.gov/eere/solar/goals-solar-energy-technologies-office
PV History in the Making – DOE SunShot Initiative
SunShot Initiative aims
  Reduce utility-scale solar electricity cost 50% between 2020 -- 2030 to $0.03 /kWh
  Address Grid integration challenges reduce market entry barriers

## Slide 11: Recent Growth in Solar
U.S. PV Electricity Installed Capacity & Generation
https://www.nrel.gov/news/press/2018/data_book_shows_continued_growth_of_renewable_electricity.html accessed 31 Jan 18
Source: DoE 2016 Renewable Energy Book

## Slide 12: Recent Solar Installation Costs
NREL PV system cost 2010–2017 summary
(inflation adjusted)
https://www.nrel.gov/news/press/2017/nrel-report-utility-scale-solar-pv-system-cost-fell-last-year.html
accessed 1/31/18

## Slide 13: PV Integration Challenges
Duck Curve
Image: http://www.caiso.com/documents/flexibleresourceshelprenewables_fastfacts.pdf
https://energy.gov/eere/articles/confronting-duck-curve-how-address-over-generation-solar-energy
High solar adoption challenges utilities to balance new grid supply and demand dynamics
Fast Gen Ramp at sunset
Overgeneration during day
PV Generators Paying for Grid Infrastructure costs

## Slide 14: Nominal PV System Overview
Shadows
Solar cell is a diode
Photon energy converted to DC
Shadows on panel & panel PV material defects non-linearly reduce energy conversion
Power Inverter converts DC to AC
Unpredictable / changing loads
Storage enables matching energy generated to energy consumed

## Slide 15: General PV Issues
PV diode
  Efficiency, cost, manufacturability, automation, testing
Packaging (encapsulation)
  Cost, weight, strength, yellowing, etc.
Accelerated life-cycle testing
  30 year outdoor test is not practical
  Damp, heat, light, immersion, etc.
Inverter & system design
  Micro-inverters, blocking diodes, reliability
  “Right sizing” components

## Slide 16: What are Solar Cells?
Current
Voltage
Open-circuit voltage
Short-circuit current
Maximum Power Point
n-type
p-type
-
+
Load
Solar cells are diodes
Light (photons) frees carriers (electrons & holes )
Resulting diode junction causes charged carrier movement
Output current is a fraction of the photocurrent
The output voltage is a fraction of the diode “built-in” voltage
+
-

## Slide 17
Standard Equivalent Circuit Model
Series
Rs
Load
Where does the power go?
Ideal Photocurrent source
Diode
(minimize)
(maximize)
Shunt
Rp
Building to this model….
Notes: 16

## Slide 18: Photon Energy
Photons characterized by  (wavelength),  (frequency), & E (energy)
In this context, energy is often expressed in electron-volts (eV), defined as 1.6 10-19 J….
Planck's constant (h): 6.626 10-34 J-s
Light’s velocity (c): 3108 m/s
Typically E (eV) & l (mm)
  … the energy gained by a single electron moving across a 1 volt potential difference

## Slide 19: Band-Gap Energy
I is free flow in conduction band
At , Metals have free s available  good conductors
  (  Metal conductivity () ↓ w/ ↑ T )
  Semi-conductors, e.g. Si, have NO free @  good insulators
FIGURE 5.4 Energy bands for (a) metals and (b) semiconductors.
Metals have partially filled conduction bands, which allow them to carry electric current easily. Semiconductors at absolute zero temperature have no electrons in the conduction band, which makes them insulators
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 20: Band-Gap Energy (cont)
  Si  ↑ w/ ↑ T; at 25oC, only 1 in 1010 in the conduction band
  Eg (band gap energy) is the energy an must acquire to transition up into the conduction band
Quantity | Si | GaAs | CdTe | InP
Band gap (eV) | 1.12 | 1.42 | 1.5 | 1.35
Cut-off wavelength (μm) | 1.11 | 0.87 | 0.83 | 0.92
Band Gap (eV) & Wavelength () Cut-offs…. Above which Electron Excitation Doesn’t Occur

## Slide 21: Silicon Solar Cell Energy Conversion Limits
AMR 1.5, Max Si PV incident energy conversion to electrical energy is 49.6%
  Photons w/  > 1.11 μm Photon energy < Eg – unavailable
  Photons w/  < 1.11 μm Photon energy > Eg – unavailable
FIGURE 5.7 Si PV Convertible Solar Energy at AM1.5
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
 > 1.11
 < 1.11

## Slide 22: Diode – Key Concepts !!
Two regions:
  “n-type” which donate electrons and
  “p-type” which accept electrons
p-n junction: free and
current readily flows in 1 direction (forward biased) but not in the other (reverse biased)
http://en.wikipedia.org/wiki/File:Pn-junction-equilibrium.png

## Slide 23: Diode – Biasing !!
  “n-type” which donate electrons
  “p-type” which accept electrons
http://en.wikipedia.org/wiki/File:Pn-junction-equilibrium.png
FIGURE 5.15
+
_
Vd
+
_
Gotta Understand the sign polarity Logic!!

## Slide 24: The p-n Junction Diode
Diode voltage-current (V-I) characteristics:
k = Boltzmann’s constant: 1.381x10-23 [J/K]
T = junction temperature [K]
Vd = diode voltage
Id = diode current
q = electron charge 1.602x10-19 C
I0 = reverse saturation current

## Slide 25: PV Cell Circuit Models
Simplest PV cell model is an ideal current source in parallel w/ a diode
Ideal source current, ISC , proportional to insolation
If insolation drops by 50%, ISC drops by 50%
ISC
Id
I
VLoad
+
I
VLoad
+
-
PV cell
Vd
+
_
_
PV cell

## Slide 26: Circuit Models of PV Cells
Using KCL
The open circuit voltage, i.e. setting I = 0 (or VLoad = )
I
ISC
Id
VLoad
+
-
Vd
+
-
The subscript SC is for short circuit

## Slide 27: PV Cell I-V Characteristic
For any ISC value, can calculate the relationship between cell terminal voltage and current (the I-V characteristics)
 PV cell I-V characteristic is the upside-down diode I-V characteristic shifted down by ISC (because I = ISC – Id)
The curve intersects the x-axis at VOC and the y-axis is ISC
-1
Isc

## Slide 28: PV Cell I-V Curves
I-V curve for an illuminated cell = “dark” curve + illuminated ISC curve
FIGURE 5.24 ISC and VOC
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
FIGURE 5.25 Photovoltaic current–voltage relationship for “dark” (no sunlight) and “light” (an illuminated cell).
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 29: PV Cell I-V Curves
More light effectively shifts the curve up in I, but VOC does not change much
By varying the insolation, we obtain not a single I-V curve, but an infinite set of I-V curves of varying with InSolation
Insolation

## Slide 30: Need for a More Accurate Model
The previous circuit is not realistic for analyzing shading effects (we’ll talk more about shading later)
Using this model, absolutely NO current can pass when one cell is shaded (I = 0)

## Slide 31: PV Equivalent Circuit
Shading has a big impact on solar cell power output… BUT it does not shutdown energy conversion!
Otherwise, a single shaded cell would force a multi-cell module’s entire output to zero.
A more accurate model includes a leakage resistance RP in parallel w/ the current source and ideal diode
  RP is large: ~ RP > 100
Series resistance, RS , accounts for V (terminal voltage) being slightly smaller than Vd
  RS is small: ~ RS < 0.01

## Slide 32: PV Equivalent with Parallel Resistor
Vd
From KCL:
For any V, adding Rp (parallel leakage resistance) reduces I by
Photocurrent source
RP
Load
(maximize)
Parallel-Only
ISC
I
V
+
-
+
-
Id
Shunt resistance drops some current (reduces output current)

## Slide 33: PV Equivalent with Series Resistor
Add series resistance Rs due to
  contact resistance between cell and wires
  semiconductor resistance
The output voltage V drops by IRs
Photocurrent source
Load
Rs
(minimize)
Series R added to ideal
ISC
Vd
+
-
V
+
-
I
Id
Series resistance reduces Vd to V at the cell terminals

## Slide 34: Series and Shunt Resistance Effects
RP – I drops by ΔI = V/RP
RP
Load
ISC
Id
I
Vd
+
_
V
+
_
RS – V drops by ΔV = I RS
Load
Rs
ISC
Id
I
Vd
+
_
V
+
_

## Slide 35: Series and Shunt Resistance Effects
Photocurrent source
RP
Load
Rs
(minimize)
(maximize)
ISC
Id
I
Vd
+
_
V
+
_

## Slide 36: General PV Cell Equivalent Circuit
The general equivalent circuit model considers both parallel and series resistance
Equivalent Circuit
Photocurrent source
RP
Load
Rs
(minimize)
(maximize)
ISC
Id
I
Vd
+
_
V
+
_
Substituting for Id and Vd
Diode equation

## Slide 37: Fill Factor and Cell Efficiency
Cell Efficiency (h) =
Voc• Isc• FF
Incident Pwr
Incident Pwr
Imax• Vmax
=
Fill Factor (FF) =
VR • IR
Voc• Isc
area = VR IR
area = Voc Isc
Fill factor is ratio at the ratio at the maximum power point

## Slide 38
Multijunction Cells
Problem: Single junction loses all of the photon energy above the gap energy.
Energy (eV)
0
20
40
60
80
100
120
140
160
180
300
500
700
900
1100
1300
1500
4.0
3.0
2.5
2.0
1.7
1.5
1.3
1.1
1.0
0.9
Intensity (mW/m2-mm)
Wavelength (nm)
Top Cell (1.9 eV gap)
Cell #2
(1.4 eV gap)
Cell #3
(1.0 eV gap)
Cell #4
(0.6 eV gap)
Solution: Use a series of cells of different gaps….
… each cell captures the light transmitted from above.
n-type
p-type
n-type
p-type
n-type
p-type
n-type
p-type
-
+
-
+
-
+
-
+
Load

## Slide 39: Record laboratory thin film PV cell efficiencies
Courtesy of the National Renewable Energy Laboratory, Golden, CO.
https://www.nrel.gov/pv/assets/images/efficiency-chart.png accessed 9 Feb 18
Notes: Notes accompanying NREL PV efficiency-chart.png
https://www.nrel.gov/pv/assets/pdfs/cell_efficiency_explanatory_notes.pdf (accessed 9 Feb 2018)
The National Renewable Energy Laboratory (NREL) maintains a plot of compiled values of highest confirmed conversion efficiencies for research cells, from 1976 to the present, for a range of photovoltaic technologies.
Devices included in this plot of the current state of the art have efficiencies that are confirmed by independent, recognized test labs (e.g., NREL, AIST, Fraunhofer) and are reported on a standardized basis. The measurements for new entries must be with respect to Standard Test or Reporting Conditions (STC) as defined by the global reference spectrum for flat-plate devices and the direct reference spectrum for concentrator devices as listed in standards IEC 60904-3 edition 2 or ASTM G173. The reference temperature is 25°C and the area is the cell total area or the area defined by an aperture.
Cell efficiency results are provided within different families of semiconductors: (1) multijunction cells, (2) single-junction gallium arsenide cells, (3) crystalline silicon cells, (4) thin- film technologies, and (5) emerging photovoltaics. Some 26 different subcategories are indicated by distinctive colored symbols.
The most recent world record for each technology is highlighted along the right edge in a flag that contains the efficiency and the symbol of the technology. The company or group that fabricated the device for each most-recent record is bolded on the plot.
The information plotted by NREL is provided in good faith, but NREL cannot accept direct responsibility for any errors or omissions. The plot is not copyrighted and may be used in presentations and publications, with a notation included that states: “This plot is courtesy of the National Renewable Energy Laboratory, Golden, CO.”

## Slide 40: Solar PV can be Quite Intermittent Because of Clouds
Image: http://www.megawattsf.com/gridstorage/gridstorage.htm
Intermittency can be reduced some when PV is distributed over a larger region; key issue is correlation across an area

## Slide 41: Silicon Solar Cell Energy Conversion Limits
AMR 1.5, Max Si PV incident energy conversion to electrical energy is 49.6%
  Photons w/  > 1.11 μm Photon energy < Eg – unavailable
  Photons w/  < 1.11 μm Photon energy > Eg – unavailable
FIGURE 5.7 Si PV Convertible Solar Energy at AM1.5
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell
 > 1.11
 < 1.11

## Slide 42: Solar Cell Efficiency
Factors that add to losses
  Electron/hole recombination
  Internal resistance
Smaller band gaps – easier e- excitation, photons w/ extra energy
   higher current, lower voltage
Higher band gaps –
   higher voltage, lower current
Thus seek middle ground,
…. usually between 1.2 and 1.8 eV
  Photons not absorbed or reflected
  Heating
FIGURE 5.9 Maximum efficiency of photovoltaics as a function of their band-gap.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 43: Maximum PV Cell Efficiency
Shockley and Queisser derived max single-junction PV cell in 1961
FIGURE 5.8 The Shockley–Queisser limit for the maximum possible solar cell efficiency (single-junction, unenhanced insolation) as a function of band-gap.
Masters, Gilbert M. Renewable and Efficient Electric Power Systems, 2nd Edition. Wiley-Blackwell

## Slide 45: US Solar Capacity
US solar capacity is growing at close to 100% yearly, with most of the growth in solar PV (as opposed to solar thermal)
Image: http://cleantechnica.com/2014/04/24/us-solar-energy-capacity-grew-an-astounding-418-from-2010-2014/
Solar PV
2004 6 GWh 2009 735 GWh
2013 8,121 GWh 2014 15,874 GWh
(about 0.4% of total)