## Slide 1
Electronic Betting System for Poker
ECE 445 – Senior Design
Spring 2019
Group 62

## Slide 2: Team introduction
Umang Chavan
Computer Engineering
Varun Pitta
Computer Engineering
Anand Giridharan
Electrical Engineering

## Slide 3: Agenda
Team Introductions | 2
Objective, Background, and Timeline | 4
Design Overview | 5
Requirements & Verifications | 9
Individual Modules | 13
Successes & Challenges | 16
Future Expansion | 17
Notes: Amaan

## Slide 4: Objective, Background, and Timeline
Phase 1
Developed circuit schematics and PCB designs
Phase 2
Tested individual modules of design (LCD, NRF24, etc.)
Phase 3
Completed and tested PCB and modules on PCB
Phase 4
Integrated player device and central hub and finished software game logic
Objective
The problem statement that we are addressing is to see if there is a more effective way of playing poker for cheap without worrying about chips
Our proposed solution is an electronic betting system that completely eradicates the need of physical poker chips
Background
Monopoly Electronic Banking Edition by Hasbro eliminated the need for paper cash that is normally used by creating a debit card system
The purpose of this was to remove the hassle of having so much paper laying around
Notes: Amol

## Slide 5: Design Overview
Notes: Amaan

## Slide 6: Physical Layout
Notes: Amol

## Slide 7: Central Unit Block Diagram
The central hub is responsible for keeping track of community game logic and also sends signals to player devices regarding the game state
Notes: Amol

## Slide 8: Central Hub Schematic

## Slide 9: Central Hub

## Slide 10: Remote Player Device Block Diagram
The player devices are controlled by the user and communicate bids and game decisions to the central hub for data management
Notes: Amol

## Slide 11: Player Device Schematic

## Slide 12: Player Device

## Slide 13: Software Flow Diagrams

## Slide 14
Software Flow Diagrams (cont.)

## Slide 15: Requirements & Verifications
Notes: Amaan

## Slide 16: Voltage Regulator Tables
Testing and validating that the voltage regulators are working properly is important for ensuring the safety of the rest of the circuit components
Expected | Output | Error
5 | 5.054 | 1.06%
5 | 5.058 | 1.14%
5 | 5.051 | 1.01%
5 | 5.045 | 0.892%
5 | 5.058 | 1.14%
Expected | Output | Error
3.3 | 3.292 | 0.243%
3.3 | 3.281 | 0.579%
3.3 | 3.301 | 0.0303%
3.3 | 3.306 | 0.182%
3.3 | 3.298 | 0.0606%
6 V Input from Battery Pack
5 V Regulator
3.3 V Regulator

## Slide 17: Functional and Integration Tests
Apart from voltage regulator tests, there were several functional tests that had to be conducted to ensure efficient flow of the game and respective devices
Transceiver Communication
1
Sent and received “Hello World” numerous time
Sent signals on different channels to different transceivers
LCD Displays
2
Display basic text for game state
Display different data on different screens (central hub)
Button Logic
3
Test if button presses change state
Correct values of bids were being altered
Game State Progression
4
Logical transitions between players accomplished
Memory saves game state on turn off/reset

## Slide 18: Individual Modules
Notes: Amaan

## Slide 19: RF Unit & Communication
The RF unit is critical for ensuring that the player device and central hub have consistent communication throughout the game
NRF24L01 Transceiver Module
Utilizes 2.4 GHz band with baud rates upto 2 Mbps
Range of up to 100 meters, more than enough for the game of poker
Can communicate with 6 other modules at the same time
1.9-3.6 V operating voltage
RC522 RFID Reader
Slave select pin allows for manual enabling/disabling
Operating frequency is approximately 13.56 Mhz
Read range for RFID tags is approximately 3cm
Data transfer rate is approximately 10 Mbps
Share same SPI bus
(MISO, MOSI, SCK)

## Slide 20: Memory Management and Atmega EEPROM
EEPROM is essential for our high-level requirement of storing data even if a device accidentally turns off or runs out of battery
The ATmega328p comes with 32k bytes Flash memory (0.5k is used for the bootloader, 2k bytes of SRAM, and 1k byte of EEPROM
Flash and EEPROM are non-volatile, therefore they persist even if power is suddenly turned off
Notes: Amol

## Slide 21: I/O Module – LCD Display
The LCD display’s are critical to both the player device and central hub because it displays the game logic and the information necessary for players to see
The V0 pin goes to the potentiometer which controls the contrast of the screen
These pins go to the ATmega328p and the signals control what is printed
There are 8 data pins, but only 4 are necessary for displaying information

## Slide 22: Successes & Challenges
Notes: Amaan

## Slide 23: Successes and Challenges of the Project
Successes
Displaying various data to different LCD screens
Saving game state to memory
Progressing game state between players
Challenges
Ensuring consistent comm. between transceivers
Handling concurrent usage of SPI bus between reader and transceiver
Maintaining physical connections due to lack of casing

## Slide 24: Future Expansion
Notes: Amaan

## Slide 25: Potential Future Expansion
After reflecting on semester’s work, these four categories are areas of improvement to consider to ensure an undisturbed game of poker
Purpose: Ensures game state is consistent and smooth experience for user
Error Handling
Purpose: Cleaner look and avoids human contact with electrical connections
Encasing
Purpose: Exploring different frequencies and/or different methods of communication
Stronger Communication
Purpose: Handling short circuits and avoiding moisture
Safety Measures
Notes: Amaan

## Slide 26
Questions?