## Slide 1
Team 46: Inventory Tracker
ECE 445: Senior Design Project Lab
Sara Alabbadi, Alex Buchheit, Sooha Ryu
April 29, 2024

## Slide 2
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING
Problem
Manual tracking of inventory is time consuming, tedious, and can create discrepancies from human error.
Solution
A system that can control user access to and update inventory as it changes can remove these errors and decrease the amount of work needed to keep track of inventory.

## Slide 3
Subsystems
Sensors – Load Cell
Locking Mechanism
User Interface
Control
Power
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Physical Design Sketch
Design

## Slide 4
GRAINGER ENGINEERING
Design
ELECTRICAL & COMPUTER ENGINEERING
Block Diagram

## Slide 5
Control access to inventory
Track total number of items in inventory
Alert system when boxes are being opened without access being granted
GRAINGER ENGINEERING
High-Level Requirements
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
GRAINGER ENGINEERING
Sensors
ELECTRICAL & COMPUTER ENGINEERING
Load Cells
Load cells in each box record the weight of the items in each box. By using the known weight of one item, the system can count the total items in each box.
Load Cell Amplifier

## Slide 7
GRAINGER ENGINEERING
Accuracy of Load Cells
ELECTRICAL & COMPUTER ENGINEERING
An important aspect of our design is the load cell’s accuracy of the output readings. According to the datasheet, the load cell should have a combined error of +/- 0.05.
Calibration Curve
Notes: Talk about repeatablity of data

## Slide 8
GRAINGER ENGINEERING
Locking Mechanism
ELECTRICAL & COMPUTER ENGINEERING
Solenoids
Unlock when correct RFID tag is scanned
Microswitch
Monitors status of box door
Will trigger alert to be displayed on user interface if a box is opened without receiving access

## Slide 9
GRAINGER ENGINEERING
User Interface: Access Control
ELECTRICAL & COMPUTER ENGINEERING
An RFID module is used to control which boxes unlock so the user can access inventory. When a user scans their RFID tag, the corresponding boxes they have access to unlock. A microswitch monitor if a box is open or closed.

## Slide 10
GRAINGER ENGINEERING
User Interface: LCD
ELECTRICAL & COMPUTER ENGINEERING
Liquid Crystal Display
Display which boxes are unlocked and if box is opened without access
LCD Pinout [1]

## Slide 11
GRAINGER ENGINEERING
User Interface: Web Database
ELECTRICAL & COMPUTER ENGINEERING
Firebase Realtime Database is chosen as our main DB
ESP32 sends required user-access log data with timestamps to Realtime database: change in number of items in each box, user ID, and accessed time
Gets total number of items in each box after each use
Constantly monitors box status

## Slide 12
GRAINGER ENGINEERING
User Interface: Website
ELECTRICAL & COMPUTER ENGINEERING
Displays RT number of items in each box
Admin can see the user access logs with a passkey, showing the userID who who accessed the inventory with the change in number of items of each box
Alert message shows up when someone "breaks in" with no access
Warning message to tell users to close the boxes after use while boxes are open

## Slide 13
GRAINGER ENGINEERING
User Interface: Website
ELECTRICAL & COMPUTER ENGINEERING

## Slide 14
GRAINGER ENGINEERING
Control
ELECTRICAL & COMPUTER ENGINEERING
ESP32-S3 Microcontroller
Controls overall flow of the locking-alarm system
Constantly monitors box status (open or close)
Controls user-access from RFID
Calculates the number of items in each inventory box
Retrieves weight in each box from the load cells
WiFi connection to allow communication to web Firebase database

## Slide 15
GRAINGER ENGINEERING
Power
ELECTRICAL & COMPUTER ENGINEERING
12 V Barrel Connector
Takes 120 V AC wall power and steps it down to 12 V DC to power solenoids
Buck Converter and Voltage Regulator
Buck converter 12 V down to 5 V to power LCD and load cell amplifiers [6]
Voltage regulator steps 5 V down to 3.3 V to power load cell amplifiers, RFID module [2]

## Slide 16
GRAINGER ENGINEERING
Challenges and Issues
ELECTRICAL & COMPUTER ENGINEERING
RFID Module
Attempted to use Parallax 28440 module
Test code available compatible with Arduino Uno
Unable to control it with ESP32-S3
Switched to RC522 module
Power System and PCB Issues
Several errors were made in PCB design
2nd wave order was pushed to 3rd wave
User Data
Need to keep user data private
Use administrator passkey

## Slide 17
GRAINGER ENGINEERING
Photos of the Project
ELECTRICAL & COMPUTER ENGINEERING
Project Setup
Main PCB
Load Cell Amplifier PCB
Open Boxes with Microswitches

## Slide 18
GRAINGER ENGINEERING
Results
ELECTRICAL & COMPUTER ENGINEERING
Successes
All sub-systems have been successfully integrated together
Load Cell Amplifier PCB
System shows potential for future applications where automatic inventory tracking is needed
System could be scaled up to integrate as many boxes as needed and with a professional packaging
Failures
Main Board PCB Design

## Slide 19
GRAINGER ENGINEERING
Future Work
ELECTRICAL & COMPUTER ENGINEERING
Future Work
Alarm system with audio sound, flash, real-time text message, etc
System could be scaled up to integrate as many boxes and registered RFID cards as needed and with a professional packaging

## Slide 20
References
[1] DeepBlueMbedded. ”ESP32 LCD Display 16×2 Without I2C – Arduino Core”. https://deepbluembedded.com/esp32-lcd-display-16x2-without-i2c-arduino/. (Accessed April 24, 2024).
[2] Diodes Incorporated. “AZ1117 LOW DROPOUT LINEAR REGULATOR WITH INDUSTRIAL TEMPERATURE RANGE .” https://www.diodes.com/assets/Datasheets/AZ1117I.pdf. (accessed Mar. 19, 2024).
[3] Espressif Systems. “ESP32-S3-WROOM-1 ESP32-S3-WROOM-1U Datasheet.” Espressif.com. https://www.espressif.com/sites/default/files/documentation/esp32-s3-wroom-1_wroom-1u_datasheet_en.pdf (Accessed Feb. 8, 2024).
[4] GitHub. ”Espressif KiCad Library”. github.com. https://github.com/espressif/kicad- libraries. (Accessed April 24, 2024).
[5] IEEE. “IEEE Code of Ethics.” IEEE.org. https://www.ieee.org/about/corporate/governance/p7-8.html (Accessed Feb. 8, 2024).
[6] Texas Intruments. "TPS56339 4.5-V to 24-V Input, 3-A Output Synchronous Buck Converter". https://www.ti.com/lit/ds/symlink/tps56339.pdf?HQS=dis-dk-null-digikeymode-dsf-pf-null-wwe&ts=1714130993240&ref_url=https%253A%252F%252Fwww.ti.com%252Fgeneral%252Fdocs%252Fsuppproductinfo.tsp%253FdistId%253D10%2526gotoUrl%253Dhttps%253A%252F%252Fwww.ti.com%252Flit%252Fgpn%252Ftps56339. (Accessed March 19, 2024).
[7] SparkFun. “PARALLEL BEAM LOAD CELL.” https://cdn.sparkfun.com/datasheets/Sensors/ForceFlex/TAL220M4M5Update.pdf. (Accessed Feb 21, 2024).
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING