## Slide 1
GymHive Tracker
Electrical & Computer Engineering
Team 28: Aryan Shah and Kushal Chava
May 6th, 2025
Notes: Aryan and Kushal

## Slide 2
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 3
What is the project?
A sensor-based system that detects machine occupancy and manages a user queue via a mobile app.
Provides real-time status updates for gym-goers and staff
Allows users to check-in to a machine using an RFID-enabled gym fob, prompting them to input their planned sets and reps
High-Level Requirements
Real-Time Equipment Monitoring: The system must accurately detect gym equipment occupancy with at least 95% accuracy (+/- 5lbs threshold for acceptance), filtering out random weight fluctuations
Efficient Data Transmission and Display: The user must be able to transmit PII (personally identifiable information) via RFID within 3 seconds of scanning a key fob. The microcontroller must process occupancy data and user check-ins within 3 seconds and transmit updated availability to the central AWS server within 1 minute of an occupancy change.
Queue Management and User Notifications: The system must estimate wait times with a maximum error margin of 20 +/- 3% by analyzing user-inputted reps and sets (high error margin due to tendency of set and rep times to vary across users)
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 4
Objective
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 5
Problem
During peak gym hours, equipment tends to get occupied quicky, leading to long wait times and disrupted workout routines
Occupied machines force gym-goers to wait or alter their routines, wasting time and undermining workout effectiveness
Solution
Real-time occupancy detection: Pressure-sensor PCBs embedded in machine pads flag when equipment is in use
RFID check-in & adaptive queueing: Users tap their gym fob, enter planned sets/reps, and the system predicts wait times
Cloud-enabled web app notifications: Web app delivers live availability updates and notifies a user when it is their turn
Problem/Solution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 6
Design Overview
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
High-Level Overview of GymHive Tracker
Visual Aid
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 8
In-Depth Overview of Custom PCB
Block Diagram
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 9
Primary Component: GHF-10 Pressure Sensor
A flexible piezoresistive polymer rated for 0 to 500 N (or 0 to ~110 lbs), mounted via a connector for easy PCB integration
Relies on a voltage divider configuration using a 100kΩ resistor, with a non-linear output that increases with added force
Interacts with our microcontroller subsystem via its ADC pins, outputting ~2.5V at 50 lbs (our threshold for a positive user detection).
Subsystem #1: Pressure Sensing Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kushal

## Slide 10
Primary Component: ESP32-WROOM-32D
The ESP32-WROOM-32D supports a variety of protocols, including built-in Wi-Fi/Bluetooth, 12-bit ADC, SPI/I2C, and GPIO interfaces
It encompasses all the protocols necessary for our design: reading the GHF-10 pressure sensor output via ADC, driving the MFRC522 RFID communication via SPI, and publishing MQTT messages over Wi-Fi to our AWS IoT Core
Subsystem #2: Microcontroller Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 11
Primary Component: MFRC522 Read/Write IC
An integrated 13.56 MHz RFID IC capable of read/write operations with a host microcontroller over SPI
Uses a 27.12MHz oscillator for operating at the desired frequency
Reads gym fobs up to 50 mm range (+/- 10mm) and transmits a unique HexCode to the ESP32
Subsystem #3: RFID Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kushal

## Slide 12
Primary Components: TYPE-C-31-M-12 USB-C & AMS1117-3.3 LDO
We provide a 5V input to our PCB via a USB-C jack from an outlet. This 5V is fed into our AMS1117-3.3V linear regulator, which steps-down the voltage to the 3.3V necessary to power the ESP32. The ESP32 then has an output rail which also feeds 3.3V, which we will use to power our peripherals.
The AMS1117-3.3V regulator works by dissipating (5V – 3.3V) * Iout as heat, which provides a stable 3.3V +/- 0.1 V under a max 500mA load
USB-C was chosen due to outlets being readily available near gym equipment
Subsystem #4: Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 13
Primary Component: HiLetgo CP2102 USB-to-TTL Adaptor
We require a PC-to-ESP32 interface for facilitating flashing C/C++ firmware and serial debugging
The USB-to-TTL adapter features a CP2102 chip that bridges USB to TTL for ESP32 programming, with data transfer happening over the TX/RX Lines
Design leveraged the ECE 445 Wiki tutorial for ESP32 USB-to-UART Programming
Subsystem #5: USB-to-UART Programming Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kushal

## Slide 14
Modifications since Design Review
Utilized HTTP API instead of REST API for gateway
Modified power source from USB-C Connector to 9V Battery
Final design utilized MFRC522 dev kit rather than IC on PCB
Instead of i-Cards, used dev kit provided RFID tags
Design Changes
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 15
Requirements & Verification
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirement | Verification Method | Result
Real-time occupancy detection with ≥95% accuracy, prioritizing 0% false negatives | We placed known weights (0–100 lbs) on the sensor and recorded ADC values at each level. We tested multiple thresholds (500, 1000, 1500, etc.) to determine which most effectively distinguished actual usage from noise, aiming to eliminate false negatives while maintaining high detection accuracy. | With a threshold of 1500: Non-occupancy detection accuracy: 100% Occupancy detection accuracy: 95% Correctly detected 19 out of 20 weight placements ≥50 lbs ✅ Requirement satisfied (≥95% accuracy for both cases)
RFID PII transmission and processing must complete within 3 seconds | Measured the total time from RFID fob tap to final display on the frontend by comparing the timestamp sent to the AWS server (from the ESP32) with the timestamp received and rendered by the frontend interface. Tests were repeated under two different backend configurations. | Result: Direct API to frontend (no DB): Avg: 1.5s, Max: 1.8s (50+ trials) API + frontend + DB write: Avg: 2.1s, Max: 2.6s (50+ trials) ✅ Requirement satisfied (under 3s in both cases)
Queue wait-time estimation error must remain within 20% ± 3% | Conducted testing with 5 users under two conditions: With sets/reps input: System predicted wait times using user-inputted workout plans. Without input: System defaulted to historical averages based on each user’s last 5 recorded durations. Compared predicted vs. actual times and calculated percentage error for both cases. | With sets/reps input: • Avg error: 10% • Correct predictions (within 20% ± 3%): 5/5 Without input (historical average fallback): • Avg error: 23% • Correct predictions (within margin): 4/5
Notes: Kushal

## Slide 16
CHART / GRAPH
GymHive Tracker Web App – Walkthrough
Software Design - Video
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Nobody

## Slide 17
Additional Software Features
User is kicked off queue after 5 minutes of inactivity
If a user who is not checked in sits down, an unknown user is pushed to the queue
Filters out random fluctuations to ensure occupancy status accuracy
Software Design - Features
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Home Page
Queue Page
Account Page
Notes: Aryan

## Slide 18
What Went Wrong
Small footprint for the USB-C Connector
  Was not stable on the PCB, fell off easily
  Difficult to resolder, required reflow oven
Not enough connectors off the ESP32 pads
  Could have integrated the MFRC522 dev kit directly to the PCB
ESP32 wasn’t reading GHF-10 input
  Pin 34 worked on breadboard but not on PCB
  Apparently because WiFi communication needed that pin
Challenges Faced
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kushal

## Slide 19
Accomplishments
End-to-End Prototype Delivered
  Custom ESP32-based PCB interfaces with AWS IoT Core in the backend and publishes data to a web app front-end interface
  All components packaged into a box with springs to aid in weight distribution for the pressure sensor
High-Level Requirements Met & Subsystems Validated
  GHF-10 was accurately able to detect occupancy
  RFID was able to detect users' check-ins using key fobs and RFID-enabled cards
  Software design allowed users to check-in, input manual reps/sets, and view a queue with an estimated wait time
What we Learned
Using datasheets to design schematics
Routing, assembling, and testing PCBs
Soldering, Reflow Oven Soldering
Engineering Design Process to Build an End-to-End Prototype
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 20
Future Work
Add IMU to each machine to remove manual input and enable automatic rep counting
Predictive analytics to train on historical durations for personalized wait-time forecasts
Perform iterative testing on proper gym equipment and gym users to gather database of information
Condensing physical design to better embed into gym equipment
Implementing Kalman filter for outliers
Future Work
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Kushal

## Slide 21
User Data Privacy and Security
By collecting and transmitting user data between the ESP32 microcontroller, AWS server, and mobile app, we put PII (personally identifiable information) at risk
  AWS IoT Core uses TLS (Transport Layer Security) to encrypt data between our ESP32 and the cloud
  Secure Account Login
Physical Safety of Equipment and Users
Embedded PCB within gym equipment points of contact can cause unintended physical hazards
  We ensure that each electrical component is securely enclosed to mitigate exposure to electrical or flammable hazards
  Our PCB operates at a low, stable voltage from 0-3.3V which reduces risks of any electric shocks or fire hazards
Ethical Concerns
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Aryan

## Slide 22
Notes: Any Questions?
TODO: Show Queue
Show Physical Design
Change Problem / Solution Pics