## Slide 1
Solar Panel Cleaner
ECE 445 Team 26
Cameron Little, Geoffrey Swisher, Thomas Cai
May 6th, 2025

## Slide 2
GRAINGER ENGINEERING
Introduction
ELECTRICAL & COMPUTER ENGINEERING

## Slide 3
Cameron Little
BSEE
GRAINGER ENGINEERING
Team Introduction
ELECTRICAL & COMPUTER ENGINEERING
Geoffrey Swisher
BSEE
Thomas Cai
BSEE

## Slide 4
GRAINGER ENGINEERING
Project Introduction
ELECTRICAL & COMPUTER ENGINEERING
ECE 469 class photo on roof of ECEB

## Slide 5
GRAINGER ENGINEERING
Objective
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
IMAGE / GRAPHIC
Dirty Solar Panels Negatively Impact Energy Production
The world is slowly adopting renewable energies: Wind, Hydro, and Solar Power
Overtime, debris accumulates on panels
How can solar array farms be efficiently cleaned?
GRAINGER ENGINEERING
Optimizing Power Output of Solar Panels
ELECTRICAL & COMPUTER ENGINEERING
[1] Mayhoub, Mohammed. (2016). Cleaning innovative daylighting systems: Review and suggested methods. Lighting Research and Technology. 49. 10.1177/1477153516669969.
A dirty and clean solar farm
Notes: Cameron

## Slide 7
GRAINGER ENGINEERING
Design Process
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
GRAINGER ENGINEERING
Original vs Final Design
ELECTRICAL & COMPUTER ENGINEERING
Original Design
Final Design
Notes: Cameron

## Slide 9
GRAINGER ENGINEERING
Final Product (spoiler)
ELECTRICAL & COMPUTER ENGINEERING
Completed project design
Notes: Cameron

## Slide 10
GRAINGER ENGINEERING
Block Diagram
ELECTRICAL & COMPUTER ENGINEERING
Notes: Geoffrey

## Slide 11
Subsystems Overview
GRAINGER ENGINEERING
Subsystems
ELECTRICAL & COMPUTER ENGINEERING
Power
Drivetrain
Controller
Cleaning Mechanism
Notes: Geoffrey

## Slide 12
Core Requirements
Ensure each voltage level has tolerance ± 10% V at no load and full load
GRAINGER ENGINEERING
Power Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Designed Voltage [V] | Used for
24 | Stepper Motor Driver (DM556T)
12 | Spinning Brush Motor
5 | Solution Sprayer Motor
3.3 | Microcontroller, IR Sensors
Can supply full load (rotating brush, spraying, and moving) without failure
Supply DC voltage levels of 24 V, 12 V, 5 V, and 3.3 V for necessary components
Full Load Voltage [V]
23.928
11.894
4.972
3.261
No Load Voltage [V]
24.147
12.061
5.032
3.270
Verification
Notes: Geoffrey

## Slide 13
Move cleaning module both horizontally and vertically across entire solar panel
Test all sides and corners to ensure full coverage of the panel
GRAINGER ENGINEERING
Drivetrain Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Initial shaft alignment test
End shaft alignment test
Core Requirements
Verification
Complete one vertical sweep in under 10 minutes
Parallel vertical stepper motors remain aligned
Use a stopwatch to measure the time
Tape the shaft and start/stop the stepper motors to see which are aligned
Notes: Geoffrey

## Slide 14
Read inputs from user interface in manual mode to control drivetrain and cleaning subsystems
GRAINGER ENGINEERING
Controller Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Core Requirements
Read inputs from IR sensors in autonomous mode and redirect drivetrain subsystem accordingly
Convert 3.3 V output logic to 5 V and 12 V for control action of sprayer and brush
Verification
Stepper motors, sprayer, and brush take action when signal is sent from microcontroller
Stepper motor changes direction when sent a LOW signal from IR sensor to microcontroller
5V/12V motor connected to Drain turns on in response to 3.3 V signal applied to Gate of MOSFET (FQP30N06L)
Logic level shifter circuit schematic
Notes: Geoffrey

## Slide 15
Core Requirements
Verification
GRAINGER ENGINEERING
Cleaning Mechanism Subsystem
ELECTRICAL & COMPUTER ENGINEERING
Must remove most of the debris without damaging the solar panel
Must operate reliably in ambient temperatures
After adding artificial debris, carefully observe and compare the condition of the solar panel before and after cleaning
Operate the cleaner outdoors under ambient temperature
Outdoor ambient temperature test
Notes: Geoffrey

## Slide 16
Our Three High Level Requirements
GRAINGER ENGINEERING
High Level Requirements
ELECTRICAL & COMPUTER ENGINEERING
1. The user can switch between manual and autonomous modes for the cleaning unit to run on without needing to restart the cycle.
2. The cleaner must complete a full vertical sweep (top to bottom and back to top) in under 10 minutes.
3. Have the cleaning system implementation work for its entirety without damaging the solar panel surface; the sprayer dispenses solution on the panel, the brush is able to spin on the cleaner unit, and the microfiber cloth picks up leftover debris.
Notes: Geoffrey

## Slide 17
PCB Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Thomas

## Slide 18
Power & Cleaning Mechanism Subsystems PCB Schematic
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Thomas

## Slide 19
Controller Subsystem (Microcontroller) PCB Schematic
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Thoams

## Slide 20
Controller & Drivetrain Subsystems (Signals) PCB Schematic
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Thomas

## Slide 21
PCB Layout
GRAINGER ENGINEERING
PCB Design
ELECTRICAL & COMPUTER ENGINEERING
Populated PCB
Notes: Thomas

## Slide 22
GRAINGER ENGINEERING
Testing
ELECTRICAL & COMPUTER ENGINEERING
Notes: Thomas

## Slide 23
Battery Powered Craftsman Weed Sprayer
GRAINGER ENGINEERING
Cleaning Solution Sprayer
ELECTRICAL & COMPUTER ENGINEERING
[2] CRAFTSMAN 1-Gallon Battery Operated Pump Sprayer (Model #CMXCAFG190640), Lowe's, https://www.lowes.com/pd/CRAFTSMAN-1-Gallon-Tank-Sprayer/1001433038
Product intended for mechanical control through hand squeezing trigger
Removed batteries; connected logic level shifter to DC pump motor for control through microcontroller
Testing
Connect terminals to 5 V supply; mimic switch to control sprayer
Measure current transients during turn on/turn off
  Iavg = 0.3 A
  Ipeak = 0.52 A
Disassembled sprayer unit
Craftsman battery powered sprayer
Notes: Thomas

## Slide 24
Infrared Break-Beam Sensors
GRAINGER ENGINEERING
IR Sensors
ELECTRICAL & COMPUTER ENGINEERING
[3] Adafruit IR Break Beam Sensor (5mm LEDs, Product ID: 2168), https://www.adafruit.com/product/2168
Emitter sends IR beam to receiver to detect a blockage between two terminals
Default output is HIGH indicating no blockage, and is LOW with a blockage.
Testing
Lab test: 48 inch separation between sensors; worked perfectly
Test on solar panel: could not sense full length of panel (48 inch)
  Sensors moved closer together and fin added to rail
IR Sensor with item blocking emitter and receiver
Notes: Thomas

## Slide 25
GRAINGER ENGINEERING
Implementation
ELECTRICAL & COMPUTER ENGINEERING

## Slide 26
GRAINGER ENGINEERING
PCB & 3D Printed Case Implementation
ELECTRICAL & COMPUTER ENGINEERING
Internal connections for case and sensors
Notes: Cameron

## Slide 27
GRAINGER ENGINEERING
User Interface
ELECTRICAL & COMPUTER ENGINEERING
User interface on custom 3D printed case
Notes: Cameron

## Slide 28
GRAINGER ENGINEERING
Powering the Moving Cleaner
ELECTRICAL & COMPUTER ENGINEERING
Coiled cable connection to brush and sprayer
Coiled cable connection to PCB
Notes: Cameron

## Slide 29
GRAINGER ENGINEERING
Powering the Moving Cleaner (zoomed out)
ELECTRICAL & COMPUTER ENGINEERING
[4] GELRHORN Coiled 3-Prong AC Power Cord, Amazon, https://www.amazon.com/dp/B0BZGTGR8T
Full view of coiled cable
Notes: Cameron

## Slide 30
GRAINGER ENGINEERING
Autonomous Mode Position Sensing
ELECTRICAL & COMPUTER ENGINEERING
Three of the IR sensors autonomous position sensors
Fin used for to determine bottom and top of panel
Notes: Geoffrey

## Slide 31
GRAINGER ENGINEERING
Manual Demonstration
ELECTRICAL & COMPUTER ENGINEERING
(click on image for video)
Notes: Geoffrey

## Slide 32
GRAINGER ENGINEERING
Automatic Demonstration
ELECTRICAL & COMPUTER ENGINEERING
(click on image for video)
Notes: Geoffrey

## Slide 33
GRAINGER ENGINEERING
Conclusions
ELECTRICAL & COMPUTER ENGINEERING

## Slide 34
Project Orientated
Miscellaneous
GRAINGER ENGINEERING
Successes
ELECTRICAL & COMPUTER ENGINEERING
Completed all three high level requirements and had a well working project
Stayed in $150 budget
Added a 3D printed case for better user interface and packaging
Large improvement between dirty and clean panel
Learned Altium Designer, 3D printing, STM microcontroller programming
3D printed case
Notes: Thomas

## Slide 35
Sprayer Inconsistencies
Sensor Sensitivity
GRAINGER ENGINEERING
Issues
ELECTRICAL & COMPUTER ENGINEERING
Tube pressure
Difference in behavior due to reservoir height
Amount of liquid dispensed
Requires unblocked line of sight
Outside interference could affect sensor detection
Glitches in sensor readings prevent immediate response
Craftsman sprayer
Sensor with “visible” IR beam
Notes: Geoffrey

## Slide 36
GRAINGER ENGINEERING
Maximum Power Point Tracking Results
ELECTRICAL & COMPUTER ENGINEERING
Power output over time during manual cleaning cycle
MPPT In Action
Dirty panel
  ~8 W of power
Clean panel
  ~54 W of power
Linear increase in power as panel is gradually cleaned
Notes: Cameron

## Slide 37
Ethics
Safety
GRAINGER ENGINEERING
Ethics and Safety
ELECTRICAL & COMPUTER ENGINEERING
Sustainability
  Help produce more green energy
Electrical safety
  Fuses; electrical tape near sprayer
Accessibility
  Easy control and autonomous mode
Mechanical safety
  Low speeds; keep distance when cleaner is running
Examples of green energy
Electrical tape used
Notes: Thomas

## Slide 38
Redesign
Future Work
GRAINGER ENGINEERING
Redesign and Future Work
ELECTRICAL & COMPUTER ENGINEERING
Change cleaning mechanisms
Change orientation of drivetrain for movement across array of panels
Determine optimal cleaning patterns and solutions
Incorporate sensors and machine learning algorithm to detect dirty sections
Solar panels on roof with accumulated dirt and pollen
Develop wireless controls
Notes: Cameron

## Slide 39
GRAINGER ENGINEERING
Any questions?
ELECTRICAL & COMPUTER ENGINEERING

## Slide 41
GRAINGER ENGINEERING
References
ELECTRICAL & COMPUTER ENGINEERING
[1] Mayhoub, Mohammed. (2016). Cleaning innovative daylighting systems: Review and suggested methods. Lighting Research and Technology. 49. 10.1177/1477153516669969.
[2] CRAFTSMAN 1-Gallon Battery Operated Pump Sprayer (Model #CMXCAFG190640), Lowe's, https://www.lowes.com/pd/CRAFTSMAN-1-Gallon-Tank-Sprayer/1001433038
[3] Adafruit IR Break Beam Sensor (5mm LEDs, Product ID: 2168), https://www.adafruit.com/product/2168
[4] GELRHORN Coiled 3-Prong AC Power Cord, Amazon, https://www.amazon.com/dp/B0BZGTGR8T

## Slide 42
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
GRAINGER ENGINEERING
Slide Title
ELECTRICAL & COMPUTER ENGINEERING

## Slide 43
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
Slide Title
ELECTRICAL & COMPUTER ENGINEERING

## Slide 44
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
Slide Title
ELECTRICAL & COMPUTER ENGINEERING

## Slide 45
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
Slide Title
ELECTRICAL & COMPUTER ENGINEERING

## Slide 46
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
Slide Title
ELECTRICAL & COMPUTER ENGINEERING

## Slide 47
CHART / GRAPH
(Short commentary or relevant information about the contents of the chart/graph.)
GRAINGER ENGINEERING
Slide Title
ELECTRICAL & COMPUTER ENGINEERING

## Slide 48
IMAGE (Send to back so Block I is not covered.)
(Text here relevant to the photo for a larger call out on a given idea or message.)
(Keep this text simple and short on one or two lines.)
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 49
IMAGE
Lorem ipsum dolor sit amet consectetur adipiscing elit
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem ipsum dolor sit amet consectetur adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 50
Lorem ipsum dolor sit amet consectetur adipiscing elit
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem ipsum dolor sit amet consectetur adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
IMAGE
ELECTRICAL & COMPUTER ENGINEERING

## Slide 51
IMAGE
(Use a photo for the entire slide like the example shown here. Send the photo to the back behind the blue shaded box. Be sure the Block I is not covered up and is in front of both the photo and blue shaded box.)
(Text here relevant to the photo for a larger call out on a given idea or message. Keep this text simple and short on one or two lines.)
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 52
(Slide the blue transparent box and the text left or right to fit over your background image. Use this text box for a call out or caption to the image.)
IMAGE
(Use a photo for the entire slide like the example shown here. Send the photo to
the back so the Block I and footer text
is not covered.)
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 53
(Closing slide option one. Suggestions for last slide)
Summary
Thank You
Questions
Contact Information
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 54
(Closing slide option two. Suggestions for last slide)
Summary
Thank You
Questions
Contact Information
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING