## Slide 1
Blade Blade
Ant-Weight BattleBot
Group 16
Sam Paone, Jack Tipping, and Patrick Mugg
December 5th, 2025

## Slide 2
High-Level Overview
BattleBots are remote-controlled combat robots that fight in an arena, and our project is an ant-weight version built to compete at the end of the semester. Because it must weigh under 2 pounds, use 3D-printed parts, include a custom PCB, and be controlled wirelessly, our design needs to balance durability, offensive power, and lightweight construction to survive the 2-minute match.
Team Goals
Build a fully functional and competition-ready ant-weight BattleBot.
Balance durability, offensive power, and lightweight design within the 2-lb limit.
Successfully integrate a custom PCB, wireless control, and all motorized systems.
Ensure stable driving, reliable weapon performance, and safe operation.
Demonstrate strong performance in the final BattleBot competition.
Introduction and Objective
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Notes: Introduction to your team and your project.
Objective. What problem are you solving?

## Slide 3
Overview of original design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 4
Initial Block Diagram
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 5
Final Block Diagram
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Buck converters must output 3.3V, 5V, and 8.4V within ±5% tolerance. | Measure each rail with a digital multimeter under load and confirm voltages stay within tolerance.
Power system must provide at least 2 minutes of continuous operation under full load. | Run the bot with both motors and saw active; confirm runtime ≥ 120 seconds before battery cutoff.
No voltage rail may exceed component max ratings under any condition. | Scope each rail during startup, sudden load change, and stall conditions to confirm no spikes occur.
Original Power Circuit
Final Power Circuit

## Slide 7
Microcontroller Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
Attack Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Servo must lift the saw assembly to at least 45° reliably under load. | Attach the full blade + motor assembly, command servo to lift, and measure angle with a protractor or digital angle gauge.
Servo must provide enough torque to lift ~2 lbs at ~10 inches, matching design expectation. | Apply a weighted force equivalent to the expected opponent lift and verify the servo can raise and hold position without overheating or stalling.
The 3D-printed mount must support the motor and blade without cracking under vibration or torque. | Run the saw at full power for 60 seconds and inspect the mount for deformation or cracks; repeat after minor impacts.

## Slide 9
Drive Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Wheel motors must drive the bot forward and backward with stable control at full battery voltage. | Power each motor through the H-bridge and verify smooth forward/backward motion on a test platform at various throttle levels.
Bot must be able to turn left and right by independently controlling wheel motors. | Command each wheel independently (one on, one off or opposite directions) and confirm the bot can achieve controlled turning on the floor.
Drive subsystem must deliver enough torque to move the fully assembled bot (~2 lb) reliably. | Place full-weight bot on test surface and verify it can start, stop, and accelerate without stalling or slipping.
Original Drivetrain Circuit
Final Drivetrain Circuit

## Slide 10
Overall System / Chassis Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Ensure Robot Chassis can withstand a force of 2lbs at a speed of 1 m/s. Additionally ensure the chassis remains at maximum .5cm off the ground to assist in defending against flipping. | Practice results of 2lb force listed above crashing into bot while moving - Practice moving the saw and trying to damage something. Try hitting the saw with 2lb of force (exact newtons listed above) to see if stays operational after words.
Once chassis assembled ensure subsystem requirements remain valid. | Reference verification of other subsystems.
Basic Model of Idea Behind Chassis, following slides have more depth

## Slide 11
Iterations on Chassis Subsystem, Initial Attempt
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 12
Iterations on Chassis Subsystem, Final Iterations
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 13
Summary of Code (Python Approach vs Arduino C Approach?)
Setup:
Initiate Bluetooth serial port
Assign output pins:
Right wheel forward pin
Right wheel backward pin
Left wheel forward pin
Left wheel backward pin
Saw motor pin
Servo PWM pin
Loop:
Read Bluetooth serial data:
'w' moves forward, 'a' turns left, 's' reverses, 'd' turns right, ' ' stops
'j' starts saw blade spin, 'k' stops
'u' lowers saw to ground, 'p' raises saw to maximum height
User Interface
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 14
Tolerance Analysis
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Component Weights
Wheel motors (2): 276 g
Saw motor: 25 g
Servo motor: 55 g
Current sensor: 5 g
Battery (500 mAh): 44 g
Subtotal: ~410 g
Chassis & PCB Allowance
Remaining weight available: ~500g
Plastic density used: 1.2 g/cm^3
Estimated chassis size: 18x18x6 cm, .5 cm wall thickness
Estimated chassis weight: ~470 g
Result:
Total estimated weight ~ 800 g, within the 2 lb limit.
Actual weight was much less as plastic sparsely filled

## Slide 15
Power Analysis
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Total Power Consumption
~193 W
Estimated Runtime
9.435 Wh / 193 W = 0.049 hours = 2.9 minutes
Reality
The estimated battery size was more than enough as the current draw estimations were worst case for each component
Subsystem Power Draw
ESP32 microcontroller: 1.65 W
Current sensor: 0.0066 W
Wheel motors (2): 44.4 W total
H-bridge (4 MOSFETs active): ~80 W
Saw motor: 16 W
Servo motor: 16.8 W
Buck converters: 34.2 W
Power Source
11.1V LiPo Battery, 850 mAh
Total energy: 9.435 Wh

## Slide 16
Video of Project
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 17
Where We Fell Short
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
System | Summary Fault
PCB | Many of the components were not soldered properly or lost H-bridge wasn’t outputting any voltage to motors Microcontroller programming circuitry didn’t function, and USB port was lost Microcontroller outputs were shorted
Chassis | Requirement on distance from floor should have been tighter Although never flipped, if flipped our chassis lacked the capabilities to return to functionality Spacing for components was tight on the inside, could've benefited from removable parts vs a chassis which was a singular print. (Partition the chassis design more)
Software | Overall, the interfacing software was great, but lacked very modular control For the most part had on and off modes, would have been interesting to have the ability to scale speed etc Also having a control panel UI which displayed battery percentage and current draw would've been a plus
Drive Subsystem | Lacked the ability to turn aggressively, partially due to tires not being pumped and therefore not able to generate the amount friction necessary to do a turn

## Slide 18
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 19
The design process is highly iterative—requiring constant prototyping, testing, revising, and repeating until a functional solution emerges.
Collaboration across mechanical, electrical, and software parts teaches the importance of clear communication and aligning designs early.
We burnt out and lost multiple parts, so it would be useful to be more careful and purchase more materials than needed
There are many unseen errors, and we should have ensured we were prepared for our deadlines a few days to a week before
We all gained experience in 3D-printing + design, programming microcontrollers, and designing PCBs
What we learned and would do differently
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING