## Slide 1: Coil Gun Control System and UI
Group 52 - Adwaita Dani, Bryan Mbanefo, Felipe Fregoso

## Slide 2: Introduction
Uses electromagnetic force to fire a projectile
Large amounts of current discharged in the windings to propel the projectile forward

## Slide 3: The Coil Gun

## Slide 4: Objectives
Control circuit for trigger timing
User Interface

## Slide 6: Projectile
Cylinder height: 2.5 cm
Outer diameter: 2.4 cm
Inner diameter: 1.6 cm
Materials: Aluminum and Copper

## Slide 7: Barrel Dimensions
Coil

## Slide 8: Trigger Circuit
Team 53’s work with the project
Need to supply them with 5V to trigger the SCRs

## Slide 9: Microcontroller ATmega328
Receive analog data from position sensor
Send digital signal to trigger circuit to discharge the capacitor
Sample data at 8 kHz
Serial communication between microcontroller and user interface

## Slide 10: Microcontroller Circuit

## Slide 11: Power - Capacitor Bank
200 V power supply to provide voltage to the 10,000 uF capacitors

## Slide 12: Power - Sensor and Microcontroller
24V power supply to LIDAR
24V to 5V buck converter for the microcontroller

## Slide 13: Power - Sensor and Microcontroller

## Slide 14: Printed Circuit Boards
Controller Board
Power Supply Board

## Slide 15: Sensor
Original sensor used three photodiodes at different points on the tube
Use time projectile passes between two sensors to calculate the velocity
Highest velocity reached was ~10 m/s

## Slide 16: Old Sensor System
Laser
Photodiode

## Slide 17: Sensor - Lidar
Pulsed laser to to that reflects of projectile to give the distance
Resolution within 0.1mm

## Slide 18: Why did we choose this Lidar?
Resolution within 0.1mm.
Variable output response time.
Analog and Switching outputs
Size/Dimensions
Ease of programmability
Measuring range of 0.05m - 10m
Output rate 1ms

## Slide 19: Sample Data from LIDAR

## Slide 20: How do we find the optimal firing position?
Optimal Stage 1, Non-optimal Stage 2
Non-optimal Stage 1, Optimal Stage 2

## Slide 21: Acceleration versus time
Optimal Stage 1, Non-optimal Stage 2
Non-optimal Stage 1, Optimal Stage 2

## Slide 22: Bullet Speed with LIDAR-based Trigger
Optimal Stage 1, Non-optimal Stage 2
Non-optimal Stage 1, Optimal Stage 2

## Slide 23: User Interface
Ease of use: Only press Fire button
Display required data as plots

## Slide 24: GUI Data Display

## Slide 25: Accomplishments
More accurate technique of measurement
Attainment of higher top speed
Creation of a platform for ease of data viewing

## Slide 26: Future Work
Documentation and instruction for firing
Create permanent product for future EOHs
Add striped bullet sensing to improve speed
Make trigger a function of both position and velocity

## Slide 27: Striped bullet diagram

## Slide 28: Special Thanks to:
Luke Wendt
Chris Barth
Scott A. McDonald
Kevin Colravy
Professor Reinhard

## Slide 29: Thank you!
Questions?