ECE 576 – Spring 2018

Homework #2		Due Tuesday, February 27, 2018

- Text problem 3.2

- Text problem 3.4

- From text equations (3.64) to (3.70) and (3.122) to (3.124), find a circuit representation for the d-axis mathematical models for standstill (zero speed).  Hint – use the idea of a common magnetizing reactance (Xmd) together with three leakage terms for the three branches with the three currents.

- The following parameters are in per unit on the base of a 555 MVA (3-phase), 24 KV (line-line), 60 Hz, 2-pole (3600 RPM) synchronous machine:

RS  = 0.003	Xls = 0.15	Xmd = 1.66

Rfd  = 0.00060	Xfd = 1.85

R1d  = 0.0062	X1d = 1.92	Cd  = 1

Neglect saturation

  - Find Xd , Xd' , Xd'' , Tdo' , and  Tdo''

  - Plot Xdop(s) as a function of frequency from .001 to 10,000 rad/sec (s=jω)

- Text problem 4.5

- Text problem 4.8