## Slide 1: Phys 102 – Lecture 6
Circuit elements: resistors, capacitors, and batteries

## Slide 2: Today we will learn about...
Circuit elements that:
Serve as conduits for charge – wires
Pump charges around – batteries
Regulate flow of charge – resistors
Store and release charge – capacitors
These elements are idealizations of components in electronic circuits & in nature
Ex: neurons, circulatory system
+
+
+
+

## Slide 3: Electric current
In electronic circuits, electrons (–e) carry current, flow opposite to current
In liquid or gas, both cations and anions can carry current
Unit: A (“Amp” or “Ampere”)
1A = 1C/s
Current – measure of flow of charge (+ charge, by convention)
Counts total charge ΔQ passing through area in a time interval Δt
I
+
+
+
+
+
+
+
Count charges through this area

## Slide 4: ACT: two light bulbs
Two light bulbs 1 and 2 are connected end-to-end by conducting wire.
If a current I1 flows through bulb 1, what is the current I2 in bulb 2?
1
2
I2 < I1
I2 = I1
I2 > I1
I1
...
...

## Slide 5: Batteries & electromotive force
Electric potential is 9 V higher at + end relative to – end. Potential difference across a circuit element is its “voltage”
+
+
–
Battery – maintains a constant electric potential difference
(“Electromotive force” – emf ε)
Electric potential difference drives current around circuit
Battery does NOT determine how much current flows
Battery does NOT generate new charges, it “pushes” charges, like a pump
9 V
I

## Slide 6: ACT: Two batteries
+
–
+
–
Two 9 V batteries are connected end-to-end by conducting wire.
What is the electric potential at point 2 relative to point 1?
+18 V
+9 V
–18 V
–9 V
1
2

## Slide 7: Resistance and Ohm’s law
Moving charges collide with each other, ions, defects inside material
Flow rate depends on electric potential difference
DEMO
Units: Ω (“Ohms”)
Potential difference causes current to flow (“downhill”, by convention)
Resistance regulates the amount of flow
+
VR
I
Double potential difference, double current
Resistance – proportionality constant between current and voltage
Ohm’s law:

## Slide 8: Physical resistance
Material
ρ (Ω∙m)
Copper 1.7 × 10–8
Iron 9.7 × 10–8
Sea water 0.22
Muscle 13
Fat 25
Pure water 2.4 × 105
DEMO
Resistance depends on material parameters and geometry
Resistor – circuit element designed to have resistance
Length – the longer the resistor, the more scattering
Cross sectional area – the wider the resistor, the more charges flow
Resistivity – density of scatterers

## Slide 9: ACT: CheckPoint 1.1
Which of the following three copper resistors has the lowest resistance?
R2
L
L
L/2
d
2d
A.
B.
C.
R1
R3
d

## Slide 10: Power generated and dissipated
Units: W (“Watts”)
1 W = 1 J/s = 1 V A
Ex: a 9 V battery does 9 J of work per 1 C of charge pumped
Battery does work pumping charges through circuit
Power – rate of energy conversion
Resistor dissipates electric potential energy
Charges lose electric potential energy in collisions inside resistor

## Slide 11: Calculation: light bulb filament
An incandescent light bulb is essentially a resistor that dissipates energy as heat and light. A typical light bulb dissipates 60 W with 120 V from an outlet.
The resistive element is a thin (40-μm diameter) filament of tungsten. How long must the filament be?

## Slide 12: Capacitance
Capacitor – circuit element that stores separated charge
Consists of two conductors separated by a small gap
Capacitance – measures the ability to store charge Q given a voltage VC applied between the conductors
Units: F (“Farad”)
1 F = 1 C/V
+Q
–Q

## Slide 13: Physical capacitance
Work to move +q from + to – plate in uniform E field (Recall Lect. 4)
Electric field is uniform between plates (Recall Lect. 3)
Field strength  density of field lines  density of charges
Capacitance depends on geometry
For a parallel plate capacitor:
Parallel plate capacitor made up of two large conducting plates of area A separated by a small gap d
–
–
–
–
–
–
–
–
–
–
+
+
+
+
+
+
+
+
+
+
A
d
Capacitor voltage

## Slide 14: ACT: Parallel plates
A parallel plate capacitor carries a charge Q. The plates are then pulled a small distance further apart.
What happens to the charge Q on each plate?
Q increases
Q stays constant
Q decreases
+
+
+
+
–
–
–
–

## Slide 15: ACT: Parallel plates 2
A parallel plate capacitor carries a charge Q. The plates are then pulled a small distance further apart.
The voltage VC between the plates
A. Increases B. Stays the same C. Decreases
+
+
+
+
–
–
–
–
DEMO

## Slide 16: Dielectrics
External field polarizes dielectric
Excess +q and –q charges build up on opposite planes
Parallel planes of +q and –q create own E field, cancel out part of external E field
Imagine placing insulating material (dielectric) between plates
(Recall Lect. 3 – conductors)
–
–
–
–
–
–
–
+
+
+
+
+
+
+
–
–
–
+
+
+
Dielectric constant κ > 1

## Slide 17: Dielectric constant κ
Since , need less E (or V) to store same Q, so C = Q/V increases:
Material
κ (> 1)
Vacuum 1 (exactly)
Air 1.00054
Rubber 3-4
Glass 5
Cell membrane 7-9
Pure water 80
Dielectric constant κ measures how much a material is polarized by electric field
Capacitance without dielectric
Capacitance with dielectric
Dielectric constant
Capacitance depends on material parameters (dielectric) and geometry

## Slide 18: Calculation: capacitance of a cell
Channels in a cell’s membrane create a charge imbalance (recall Lect. 5), with + charge outside, – inside. The separated charge gives the cell capacitance, with the membrane acting as a dielectric (κ = 7).
Based on EXAM 1, FA09
What is the capacitance of a 1-μm2 flat patch of cell?
6 nm
Voutside = 0
Vinside = – 70mV
At rest, a cell has a –70 mV voltage across it. How much charge is necessary to generate this voltage?
κ = 7
+Q
–Q
=

## Slide 19: Capacitor energy
Separated charges have potential energy (Recall Lect. 4)
Important factor of ½! Don’t confuse this equation with U = qV for individual charge q
Defibrillator
Lightning strike
Camera flash
Why separate charge?
A way to store and release energy

## Slide 20: ACT: Capacitor dielectric
A parallel plate capacitor carries a charge Q. A dielectric with κ > 1 is inserted between the plates.
What happens to energy UC stored in the capacitor?
UC increases
UC stays constant
UC decreases
+
+
+
+
–
–
–
–
κ > 1

## Slide 21: Summary of today’s lecture
Batteries generate emf ε, pump charges
Resistors dissipate energy as power: P = IV
  Resistance: how difficult it is for charges to get through: R = ρL/A
  Voltage determines current: V = IR
  Ideal wires have R = 0, V = 0
Capacitors store energy as separated charge: U = ½QV
  Capacitance: ability to store separated charge: C = κε0A/d
  Voltage determines charge: V = Q/C
Don’t mix capacitor and resistor equations!