## Slide 1: Phys 102 – Lecture 7
Series and parallel circuits

## Slide 2: Today we will...
+
+
Learn about electric circuits
    Circuits with a battery, wires, and resistors
    Circuits with a battery, wires, and capacitors
Analyze circuits
  Take a complex-looking circuit like...
  ...and turn into a simple-looking circuit like

## Slide 3: Recall from last time...
Electric potential difference across circuit element is its “voltage” Velement
Should be “ΔV”, but we’ll usually drop the “Δ”
Resistors – regulate current
Dissipate power
R
Capacitors – store charge
Store energy
C
+
Batteries – pump charges
Provide emf for charges
ε
Circuits connect elements with wires, which we treat as ideal conductors

## Slide 4: Kirchhoff loop rule
+
A charge making a complete loop around a circuit must return to the same electric potential (“height”) at which it started
Battery
(pump)
Resistor R
(bumpy hill)
+
ε
VR
Sum of electric potential differences (voltages) around circuit loop is zero
ε
R

## Slide 5: Series components
Two components are said to be in series when they are connected end-to-end by a single wire
V1
ε
V2
+
ε
R1
R2
R1
R2
I1
I2

## Slide 6: ACT: CheckPoint 1.2
V1 > V2
V1 = V2
V1 < V2
+
R1 = 1 Ω
R2 = 10 Ω
ε
Consider a circuit with two resistors R1 and R2 in series. Compare the voltages across the resistors:

## Slide 7: ACT: Capacitors in series
+
ε
Consider a circuit with two capacitors C1 and C2 in series. Compare the voltages across the capacitors:
V1 > V2
V1 = V2
V1 < V2
C1 = 1 μF
C2 = 10 μF

## Slide 8: Equivalent resistance & capacitance
Circuit behaves the same as if series components were replaced by a single, equivalent component
R1
R2
Resistors
Capacitors
=
=
Req
C1
C2
Ceq
V1
V2
Veq
V1
V2
Veq
Ieq
I2
I1
Q1
–Q1
Q2
–Q2
Qeq
–Qeq
Notes: Demo – 512 & 164 Resistors/capacitors in series and parallel

## Slide 9: Calculation: vascular resistance
Pressure difference
Blood flow
Vascular resistance
emf
Electric current
Electrical resistance
The circulatory system is analogous to an electric circuit
The circulatory system consists of different types of vessels in series with different resistances to flow
*Numbers represent accurate relative values
Artery
Arteriole
Capillary
Venule
Vein
εheart = 120 V*
RA = 20 Ω
Ra= 50 Ω
Rc = 20 Ω
Rv = 6 Ω
RV = 4 Ω

## Slide 10: Calculation: vascular resistance
εheart = 120 V
RA = 20 Ω
Ra = 50 Ω
Rc = 20 Ω
Rv = 6 Ω
Calculate the current I through the vascular circuit and the voltages across the different types of vessels
RV = 4 Ω
Artery
Arteriole
Capillary
Venule
Vein
Simplify
εheart
Req
Expand

## Slide 11: Kirchhoff junction rule
–
+
+
+
+
Junction
Charges flowing through a junction split. By conservation of charge, the sum of currents into a junction equals the sum of currents out of a junction
+
+
+
I3
I2
I1
I1
I2
I3

## Slide 12: Parallel components
ε
V1
V2
Components are said to be in parallel when both ends are connected to each other, forming a loop containing only them
+
ε
R1
R2
I2
I1
I
I1
I
I2

## Slide 13: ACT: Parallel or series?
+
Consider the circuit to the right. Which of the following statements is true?
C1 & C4 are in series
C2 & C4 are in parallel
C1 & C3 are in parallel
ε
C2
C4
C1
C3

## Slide 14: ACT: Resistors in parallel
R1 = 1 Ω
+
Consider a circuit with two resistors R1 and R2 in parallel. Compare I1, the current through R1, to I2, the current through R2:
R2 = 10 Ω
ε
I1 > I2
I1 = I2
I1 < I2

## Slide 15: ACT: CheckPoint 2.3
R1
+
R2
ε
Now we add a switch S. What happens to the current out of the battery when the switch is closed?
Ibattery increases
Ibattery remains the same
Ibattery decreases
DEMO
S
Notes: Demo 1091 – blow the fuse

## Slide 16: Equivalent resistance & capacitance
Circuit behaves the same as if parallel components were replaced by a single, equivalent component
R1
R2
Resistors
Capacitors
=
=
Req
C1
C2
Ceq
V1
V2
Veq
V1
V2
Veq
Ieq
I2
I1
Q1
–Q1
Q2
–Q2
Qeq
–Qeq
Notes: Demo – 512 & 164 Resistors/capacitors in series and parallel

## Slide 17: Calculation: vascular resistance
In previous calculation, capillaric resistance accounts for ~20% of total vascular resistance, yet capillaries are the thinnest blood vessels, and should have the highest resistance. Why?
Artery
Capillary
Venule
Vein
Arteriole

## Slide 18: Calculation: cardiovascular system
Rbrain
Rpulm
Rbody
εheart
+
The human cardiovascular system consists of two circuits: pulmonary circulation which carries blood though the lungs, and systemic circulation which carries blood to the organs
Calculate current through each component of circulatory system
Rpulm = 12 Ω, Rbrain = 1 kΩ, Rbody = 160 Ω, εheart = 120 V
The organs of the body are connected in parallel in the systemic circuit
Simple circuit model*:
*Numbers represent accurate relative values
Notes: Technically right and left ventricles are batteries in series flanking lungs – we’ll combine them into one battery
Rlung = 1.1x10^4 Pa s/l
Raorta = 107 Pa s/l
Rbrain = 1.025 x 10^6 Pa s/l
Rtot = 1.4 x 10^5 Pa s/l (from isnap.nd.edu/Lectures/mphysics)
Rpulmonary = 2-13 Mpa s/m^3 (Pulmonary vascular resistance PVR)
Rsystemic = 70-160 MPa s/m^3 (Systemic vascular resistance SVR) (wikipedia vascular resistance)

## Slide 19: ACT: analyzing circuits
Which of the following circuit is different than the others?
I
II
III
Circuit I
Circuit II
Circuit III
All three are equivalent
All three are different
+
+
+

## Slide 20: Calculation: circulatory system
+
Rpulm = 12 Ω, Rbrain = 1 kΩ, Rbody = 160 Ω, εheart = 120 V
Calculate current through each component of circulatory system
Rbrain & Rbody are in parallel
Rpulm & Rsyst are in series
Simplify
Simplify
Rbrain
Rpulm
Rbody
εheart
+
Rpulm
Rsyst
εheart
+
Rtot
εheart

## Slide 21: Calculation: circulatory system
+
Expand
Rpulm & Rsyst are in series
Rpulm = 12 Ω, Rbrain = 1 kΩ, Rbody = 160 Ω, εheart = 120 V
Calculate current through each component of circulatory system
Rtot
εheart
+
Rpulm
Rsyst
εheart

## Slide 22: Calculation: circulatory system
+
Expand
Expand
Rbrain & Rbody are in parallel
Rpulm = 12 Ω, Rbrain = 1 kΩ, Rbody = 160 Ω, εheart = 120 V
Calculate current through each component of circulatory system
Rtot
εheart
+
Rpulm
Rsyst
εheart
+
Rbrain
Rpulm
Rbody
εheart

## Slide 23: Summary of today’s lecture
Two basic principles:
Kirchhoff loop rule
  Voltages around circuit loop sum to zero (based on conservation of energy)
Kirchhoff junction rule
Currents into a circuit branch equal currents out (based on conservation of charge)

## Slide 24: Summary of today’s lecture
Series components
  Currents are the same
  Voltages add
  Resistors Capacitors
Parallel components
  Voltages are the same
  Currents add
  Resistors Capacitors
Don’t mix equations!