## Slide 1
Lecture 24: Topological qubits and Majorana fermions
Lecture 23: Decoherence and the Transmon qubit
Next time
Today
Discussion of applications of superconductor materials and devices in five parts:
Overview of the quantum information landscape
Macroscopic quantum phenomena in superconductor devices and superconductor qubits
Decoherence and the emergence of the transmon qubit
Topological superconducting qubits based on Majorana fermion states
S-TI-S Josephson junctions --- a compelling platform

## Slide 2
Final project
6 groups + individual papers
Explore a topic --- make a set of slides
12 minute presentation on Tuesday, May 10 (last day of class)
Topics:
Conventional SC qubits vs. topological SC qubits
SC qubits vs. ion trap qubits
SC qubits vs. semiconductor qubits
Quantum Supremacy
Superconductors for Quantum Sensing
Quantum computing for discovery of new superconductors
Goal is for everyone to participate --- I would suggest that your team make a plan and have each person contribute some specific component or specific slides to the presentation
Very unstructured open-ended assignment
Will need to explore the internet to find interesting materials and converge on a theme and focus for your presentation
Emphasis is on learning something and sharing that with all of us --- to me, this assignment will be successful if we all learn some new things and come away with a picture of the potential and challenges of superconductivity in quantum information science and technology

## Slide 3
Conventional SC qubits vs. topological SC qubits | SC qubits vs. ion trap qubits | SC qubits vs. quantum dot or semiconductor qubits
Abboud, Nick | Birchmier, Rachel Lucille | Fu, Wenning
Beach, Alexander R | Rooke, Spencer George | Ganesan, Vishal
Song, Xiangyu | Wild, Drew Glenn | Peng, Yu-Ting
Suresh Babu, Soorya | Wu, Junyi | Wu, Dufei
Quantum Supremacy | Superconductors for Quantum Sensing | Quantum computing for the discovery of new superconductors/materials
Gabrisko, Nick | Hu, Yuxuan | Apte, Sohm Shailesh
Kim, Dong Beom | Tsai, Pei-Wen | Vaz, Daniel Edward
Montone, Jessica H |  | Zhang, Michael
Wang, Ningdong |  | Zvenigorodsky, Serge
RESEARCH PAPERS |  | 
 | Agrawal, Shraddha | 
 | Baker, Carina Franziska | 
 | Lennox, Amber Rose Elizabeth | 
 | Lin, Haoran | 
 | Ma, Max | 

## Slide 4
Superconductor qubits
Macroscopic Quantum Phenomena --- ways in which SC devices behave as quantum mechanical objects
Types of superconductor qubits
charge qubits
phase qubits
flux qubits
hybrid charge-phase qubits (one example is the transmon qubit)
Decoherence
  Characterization T1, T2
  Sources of decoherence
  Reducing decoherence
Transmon qubit --- developed to avoid decoherence
Verified qubit operation (superposition of quantum states)
How good does it need to be to do “quantum computing”?

## Slide 6: Sources of Decoherence
phonons
photons
charge fluctuations
paramagnetic/nuclear spins
magnetic-field noise
critical current fluctuations from charges
quasiparticle tunneling
environment circuit modes
dielectric losses
Bottom line is that anything and everything matters --- and if does not now, it will at some point as circuits scale in size and complexity

## Slide 7: Sources of low frequency noise in superconducting qubits
Critical current noise … charge motion
Flux noise … vortex motion
Magnetic moments and/or vortices hopping in SC film induces flux changes in qubit loops
dominates for large loops
and large junctions
Charge trapping in Josephson junction barrier blocks tunneling in localized region  change in critical current
dominates for small loops
and small junctions
Example: charge traps in tunnel junctions
(Wakai, Van Harlingen)
Single vortex/charge trap creates switching noise  Lorentzian in power spectrum
Multiple vortices/charge traps add to give ~1/f noise spectrum (Dutta-Horn model)

## Slide 8
Effect of low frequency noise on the measurement of coherent quantum oscillations
IC
IC
rf SQUID qubit
L
I
1/f flux noise in qubit and coil current noise modulates flux bias
from ½ 0
1/f critical current noise modulates tunneling barrier height
 ~ ()2

Fluctuation of the tunneling frequency causes phase noise  results in an effective decoherence since  is different for each successive point of a distribution measurement
t

dephasing factor:
 ~ Ic

## Slide 9
Effect of critical current fluctuations on tunneling frequency
 = 20.4
 = 19.3
 = 40.6
 = 1.0

## Slide 10
Determining the decoherence time from 1/f noise
Assume a measurement of the coherent oscillations in a qubit

t
ave
tf
ss = single shot flux sampling time (~ 1ms)
Nss = number of flux samples at each time (> 1000)
Np = number of time points to map oscillations (> 100)
N = Nss x Np = total number of measurements (> 105)
N ss = total measurement time (> 100s)
Put in 1/f critical current noise with spectrum appropriate to the measurement scheme:
Determine decoherence time  limited by dephasing

## Slide 11
Numerical simulation
Assume a 1/f critical current noise spectrum:
Generate critical current fluctuation distribution:
Example:
Calculate flux oscillations averaged over the ensemble of measurements:
  450ns
Ic = 1 A
/2 = 10 GHz
 = 10

## Slide 12
General expression: decoherence from 1/f critical current noise
1/f critical current noise:
decoherence time:

## Slide 13
Qubit parameters and predicted performance (T=100mK)
Conclusion: Predicted decoherence times from 1/f noise are longer than what has been obtained by measurements (<< 1s) but could become a limiting problem in the future (similar study and conclusion for flux noise)
~2005

## Slide 14: Superconducting Qubits Taxonomy and Evolution
Flux qubits
Phase qubits
Flux-biased Phase QB
(NIST)
C-shunted, Flux-Biased Phase Qubit
(NIST, UCSB)
3JJ Persistent-current QB
(Delft, MIT, NEC, NTT)
RF SQUID Qubit
(Stony Brook)
C-Shunt 3JJ Qubit
(RIKEN, IBM, MIT)
4JJ Qubit
(Delft, IBM)
Double degeneracy CPB
(Quantronium, Saclay)
C-shunt CPB (2D Transmon, Yale, …)
Charge Qubits
Cooper Pair Box (CPB)
L-shunted RF SQUID
(JJ-string inductor, Fluxonium, Yale)
C-shunt CPB in 3D cavity (3D Transmon, Yale)
L-shunted RF SQUID
(nanowire inductor, metastable, MIT/LL)

## Slide 15
Transmission line + plasmon = “transmon”

## Slide 20
Measure the qubit using microwave
Continuous microwave is controlled by mixer to form microwave pulses
The output signal is mixed with another frequency microwave then filtered to generate measurable signal in MHz range.

## Slide 21
Two transmons coupled via a resonator
Di Carlo et al, Nature 2009

## Slide 25: Shunt Capacitor Loss & Participation
“2D” Transmon
Large plates form capacitance through the large cavity, predominantly vacuum. T1 in range 10-100 us. The cost is a much larger form factor for the device (cm size)
“3D” Transmon
Electric field
H. Paik et al., PRL 107, 240501 (2011)
CS dominates the capacitance
Most capacitive energy is stored in CS
 CS has the largest “participation”
Options:
1) improve materials  reduce loss
2) reduce E-field density in lossy region
How lossy is the shunt capacitor Cs?
Planar inter-digitated capacitor (IDC) loss put T1 ~ 1-10 us.
Today, materials improvements put T1 ~ 50 us.

## Slide 26: Superconducting Qubits: Remarkable improvements in qubit coherence
“Moore’s Law” for T2
Oliver & Welander, MRS Bulletin (2013)
Blue: MIT & LL
lowest thresholds
for quantum
error correction
several groups 100-150 us
(Delft, IBM, MIT, Yale, …)
NIST/IBM, Yale, ...
MIT-LL Nb Trilayer
Remarkable improvement in T1,2 by groups worldwide
  Materials
  Fabrication
  Design
Major qubit types (times at MIT)
  Flux qubit: T2 = 23 us
  2D transmon: T2 = 35 us
  3D transmon: T2 = 150 us
  C-shunt flux qubit: T2 = 100 us
Applications
  Gate-based quantum computing
  Quantum annealing
Five orders of magnitude improvement in T2 over the past 15 years by groups worldwide.

## Slide 28
Pulse generation
Cryostat input
Cryostat output
Physics
Data acquisition
Measurement Chain

## Slide 29
Classical to Quantum to Classical Interfaces

## Slide 30
Statement
Qubit control - applying qubit drive tones
In the rotating frame of the qubit, we can show that its drive Hamiltonian can be written
where the pre-factor is the pulse envelope
Pulse duration, [ns]
State pop. [a.u.]

## Slide 31
Dispersive readout
Jaynes-Cummings Hamiltonian
Resonator
Qubit
Interaction
A. Blais, et al. Phys. Rev. A, 69, 062320, (2004)
Dispersive frequency shift
Dispersive regime:
Map of quantum properties to microwave response
Conclusion
All we need to do now is to measure the resonator response to find out the qubit state.

## Slide 32
Resonator drive tone
To read out the qubit state, we send a readout pulse to the resonator at a fixed frequency
Dispersive readout
Maximum state discrimination when biased just in between the two S-curves.

## Slide 33
Google

## Slide 34
IBM