## Slide 1: Physics 598 BP: Experimental Biophysics
Paul Selvin (Instructor—Lectures)
(Usually) Monday 4-5pm, 322 LLP
This week only: Tuesday and Thursday, 1-3 pm (or-so)
Jaya Yodh (Instructor – Labs)
(knows everything): Bright-field Microscopy
Marco Tjioe, Duncan Nall, Yuji Ishitsuka – TA (Selvin)
ensemble Fluorescence, FIONA, PALM/ STORM
Jaba Mitra –TA (Ha group)
smFRET

## Slide 2: What we’re here for
Give you direct experience in lab manipulations associated with modern biophysics
I’m sort of irrelevant!
We are not here to lecture you!
A big part is you must take responsibility for learning
We’re here to help.
Model is based on summer schools,
Taught for past 5 years, about 40 students/year,
1 week/year, very full-time.
1 TA every 3 (or 4 students)
A big emphasis will be on detection via
Fluorescence and Single Molecules

## Slide 3: Physics 598BP—look at Lab handout
Format: 5 experimental labs will be offered in total, each being 3 week, with 1 week being only 2sessions in a week. M 4-5pm lecture
Ensemble Fluorescence (Location - Loomis Selvin Lab; Instructor(s) - Marco Tjioe Part 1: Dye absorption, emission, lifetime, anisotropy; Part 2: Bulk FRET, donor-acceptance donor
Bright Field & Fluorescence Microscopy (Location – IGB; Instructor - Jaya Yodh)
smFRET (Location – Loomis Ha Lab; Instructor -Jaba Mitra)
Special two week lab section –extra night class required!
FIONA (Location - Loomis Selvin Lab; Instructor(s) - Marco Tjioe)
STORM/PALM (Instructors – Duncan Nall and Yuji Ishitsuka (Selvin lab))
Light Sheet Microscopy or Optical Trap (Location – IGB, Instructor Duncan Nall or Roshni Bano (Chemla Lab).
1 week demo only.
You must choose a lab time, Tuesday or Thursday

## Slide 4: Grades
Not a big emphasis
Do labs, reading.
Turn in the lab reports (on time)
with everything done.
Do individual presentation at end.
No tests.

## Slide 5: Our Web site: http://courses.physics.illinois.edu/phys598bp/ Lab Handouts (Lab 1 or 2, read by Tuesday) “Visualizing Cells” READ by Monday! Really good Web sites Florida State University http://micro.magnet.fsu.edu/primer/ (Olympus) http://zeiss-campus.magnet.fsu.edu/articles/basics/index.html (Zeiss) Molecular (or Essential) Biology of the Cell http://www.ncbi.nlm.nih.gov/books/NBK26880/ Wikipedia
Good Resources

## Slide 6: Lab 1: Bright Field and Fluorescence Optical Microscopy and Sectioning
Ensemble Fluorescence (Location - Loomis Selvin Lab; Instructor(s) - Marco Tjioe and/or another Selvin student)
Part 1: Dye absorption, emission, lifetime, anisotropy
Part 2: Bulk FRET, donor-acceptance donor
Bright Field & Fluorescence Microscopy (Location – IGB; Instructor - Jaya Yodh)
Part 1: Brightfield, Kohler illumination DIC, Phase Contrast, Color, Fluorescence Microscopy
Part 2: Widefield fluorescence 3D stack and deconvolution

## Slide 7: We’re going to cover here: Lab 2: Bright Field and Fluorescence Optical Microscopy and Sectioning
(1) Basic Concepts in Microscopy
• Magnification
• Numerical Aperture and Resolution
• Point Spread Function and Deconvolution
(2) Bright Field Imaging
• Köhler illumination
(3) Enhancing Contrast in Optical Microscopy
• Phase Contrast Bright Field Imaging
• Differential Interference Contrast (DIC)
(4) Fluorescence Imaging
(5) 3D-Imaging of thick specimen
• Z-stack wide-field fluorescence Imaging and deconvolution

## Slide 8: Introduction to seeing

## Slide 9: Lens Maker Equation (for thin lenses)
http://en.wikipedia.org/wiki/Lens_(optics)
A lens transfers an object plane to an image plane with some magnification.
An image is formed where one object point goes to one (and only one) image point.
o
i
o
i
i
o
Different lenses,
depending on curvature, have different magnification
4x  100x
Def’n: Object and image planes are conjugate planes.
What is object has finite thickness? Do you have problems?
In 3D, you have problems with out of focus light. (Need Deconvolution microscopy)

## Slide 10: Numerical Aperture Objective lens does this with some magnification and collecting some fraction of the emitted/scattered light Numerical aperture = NA = nsinq n = Index of refraction of media (n= 1.0 air; 1.33 water; 1.5 for immersion oil)
Higher N.A., can detect weaker fluorescence (highest NA= 1.49-1.68)
media
Also, higher NA gives you better Resolution
Resolution ~ _l _
2 NA

## Slide 11: Bright-field Microscopy is the most common type of microscopy (often with dyes)
Clubmoss (Lycopodium) Strobilus
Approximately 200 different species of primitive vascular plants commonly referred to as clubmosses are classified in the genus Lycopodium. The pollen produced by the plants is flammable and was formerly utilized as a flash powder for early cameras and as a common component of fireworks
http://www.olympusmicro.com/primer/anatomy/brightfieldgallery/index.html
Simple. Microscope is straightforward
Light source (bulb),
sample, detector.
Does the job.

## Slide 12
Microscopes
Cells discovered with invention of microscope.
1000x, 0.2 um
Or with CCD
Molecular Biology of the Cell. 4th edition.
Alberts B, Johnson A, Lewis J, et al.
New York: Garland Science; 2002.
Resolution: ability to spatially differentiate two dyes, related to wavelength and numerical aperture.
Resolution = l/[ 2 N.A. ]

## Slide 13: (Side-point) Objective Lenses: Infinity corrected (now standard, greater flexibility)
Optical elements (filters, etc.)
Detector
Tube lens
Fixed length (160-220 mm, depending on company)
Infinity space
object
image
Object

## Slide 14: Brightfield Microscopy vs. Dark-Field (Fluorescence) Microscopy
http://www.olympusmicro.com/primer/anatomy/brightfieldgallery/index.html
Brightfield
Fluorescence
Dark-Field much more sensitive!
Requires changing of optics and new labels

## Slide 15
Brightfield Microscope
Brightfield: you have light (excitation source) shining on sample and going into your eye. Signal is when you absorb some of light. Have to see the difference between light and (light-absorption).
How to make it dark-field?

## Slide 16: Bright-field is inherently less sensitive than dark-field (fluorescence)
If you have no (or less) background, easier to measure
-- lots of contrast
e.g. measure some hair: two ways: 1) take some hair and weigh it. 2) take my whole body with hair, weight it; chop of the hair, and weigh body again, and take difference.
Which is more sensitive?

## Slide 17: Darkfield Microscopy (Fluorescence is just one type of dark-field microscopy) Great technique if it works
Propagation of incoming light
No light hitting specimen. Non-diffracted (bent) waves do not get detection, i.e. dark-field

## Slide 18: Fluorescence Microscopy
What is it? How does it compare in sensitivity to brightfield?
Background is potentially ZERO!
With little background, can see very little
Stokes Shift (10-100 nm)
Excitation
Spectra
Emission
Spectra
Light In
Light Out
Most objects do NOT fluoresce.
3 nm (small)

## Slide 19: Microscopy: how well can you resolve two things
Can resolve things to (ideally) l/2N.A.
Electron Microscope can get better resolution mostly because it has smaller wavelength.
~200 nm
visible light
Single-molecule
Microscope
We’ll spend much time with SMM!

## Slide 20
(old technique)
A. Critical Illumination. Conjugate planes are the illuminating bulb filament and sample plane (O). When adjusted correctly, the image of the filament is seen coincident with the sample image. A diffusing glass filter (d) is used to blur the filament image.
FD: Field diaphragm: CD: Condenser diaphragm
B. Köhler Illumintion: Conjugate planes are the illuminating bulb filament and Condenser diaphragm. Second conjugate planes are the Field diaphragm and the sample plane. When adjusted correctly, the image of the field diaphragm and the sample are coincident. The filament is out of the plane of focus, and thus uniformly diffuse.
Brightfield: Köhler illumination (invented 1893):
Makes illumination uniform
(used with sources like light bulbs; irrelevant for lasers)
http://microscopy.berkeley.edu/courses/tlm/condenser/optics.html
The trick is to make sure that you are not imaging the light source. The filament is out of the plane of focus, and thus uniformly diffuse.

## Slide 21: Accuracy and Resolution and Diffraction Effects Why resolution is l/2 N.A. Limit to how sharply you can image

## Slide 22: Point Spread Function Even a “point” forms a finite spot on detector. No matter how small an emitting light, it always forms a finite-sized spot, PSF ~ l/2NA You can “never” get better than l/2NA ~ 500 nm/2* 1.4 ~ 175 nm
PSF depends on NA
(Caveat: can do 100x better with single molecules!)

## Slide 23: Resolution: The Abbe or Rayleigh criteria
How well can you resolve two nearby (point) objects?
The resolution is limited to how well you can separate two overlapping PSFs.
Light always spreads out to ~ l/2NA
Rayleigh Criteria ~ ~ l/2NA ~ 200-250 nm
We will overcome this limit through single molecule imaging!

## Slide 24: Point Spread Function If you don’t have a point emitter, but one that has a z-component, you also have a PSFz.
http://olympus.magnet.fsu.edu/primer/digitalimaging/deconvolution/deconintro.html

## Slide 25: Deconvolution Microscopy
PSF has not only an x,y component, but also a z-component. You see in x-y, but this is the x-y from a whole bunch of z emitters.

## Slide 26: Deconvolution: better images
http://media.materialsviews.com/wp-content/uploads/2012/01/BX3-and-Deconvolution.jpg

## Slide 27
What if you can’t see something
by change in amplitude?
Light has a phase, (plus an amplitude)
You may be able to see a phase change.

## Slide 28: Bright-field Microscopy –Phase Contrast Limits to sensitivity
Have to interfere with each other,
i.e. end up hitting detector at same place.
N photon
Detector
+f
sin wt
A sin wt + f
Asin wt

## Slide 29: Two related (but different Techniques) Phase Contrast & Digital Interference Microscopy
http://micro.magnet.fsu.edu/primer/techniques/dic/dicphasecomparison.html
DIC
Phase
Contrast
a thick section of murine kidney tissue
Confusing
Nuclei visible

## Slide 30: Two Phase Techniques: Phase Contrast and Differential Interference Contrast (DIC, Nomarski) Microscopy. Both rely on phase difference between the sample and background, yet give quite different signals
DIC: optical path length gradients are primarily responsible for introducing contrast into specimen images: Really good for edges. Thick samples; can be used with high numerical aperture lenses
Phase contrast yields image intensity values as a function of specimen optical path length magnitude, with very dense regions (those having large path lengths) appearing darker than the background. Alternatively, specimen features that have relatively low thickness, or a refractive index less than the surrounding medium, are rendered much lighter when superimposed on the medium gray background.
Good for thin samples.
http://micro.magnet.fsu.edu/primer/techniques/dic/dicphasecomparison.html

## Slide 31: Phase Contrast Microscopy
Very little absorption, so Brightfield and Darkfield isn’t good.
Phase contrast is an excellent method to increase contrast when viewing or imaging living cells in culture, but typically results in halos surrounding the outlines of edge features.
The technique is ideal for thin unstained specimens such as culture cells on glass.
(which are approximately 5 to 10 micrometers thick above the nucleus, but less than a micrometer thick at the periphery), thick specimens (such as plant and animal tissue sections).
Slight differences in phase are translated into differences in intensity
The amount of the phase shift depends on what media (refractive index) the waves have passed through on their paths, and how long the paths were through these media.
Notes: The technique is not useful for thick specimens (such as plant and animal tissue sections). because shifts in phase occur in regions removed from the focal plane that distort image detail. Furthermore, floating debris and other out-of-focus phase objects interfere with imaging adherent cells on coverslips.

## Slide 32: Phase contrast microscopy
Notice red line, which contains a different phases due to sample is not phase shifted. They interfere with light that is unrefracted.

## Slide 33: Differential Interference Contrast Microscopy
Differential interference contrast microscopy requires plane-polarized light and additional light-shearing (Nomarski) prisms to exaggerate minute differences in specimen thickness gradients and refractive index. Good for thick samples.
Can use high numerical apertures (in contrast to Phase contrast).
Lipid bilayers, for example, produce excellent contrast in DIC because of the difference in refractive index between aqueous and lipid phases of the cell. In addition, cell boundaries in relatively flat adherent mammalian and plant cells, including the plasma membrane, nucleus, vacuoles, mitochondria, and stress fibers, which usually generate significant gradients, are readily imaged with DIC.
Notes: Differential interference contrast is an important technique for imaging thick plant and animal tissues because, in addition to the increased contrast, DIC exhibits decreased depth of field at wide apertures, creating a thin optical section of the thick specimen.

## Slide 34: Nomarski or differential interference contrast (DIC) microscopy Bright-field, polarization sensitive, see diff. around the edges
You see something only if it changes the angle of polarization

## Slide 35
Class evaluation
1. What was the most interesting thing you learned in class today?
2. What are you confused about?
3. Related to today’s subject, what would you like to know more about?
4. Any helpful comments.
Answer, and turn in at the end of class.

## Slide 36: The End